## Slide 1
info@3E.eu
Validation of mesoscale generalisation procedure for the WRF model
Andrea N. Hahmann (DTU)
Grégoire Leroy (3E)
Rory Donnelly (3E)
David Schillebeeckx
Notes: My presentation will cover the post-processing of WRF simulations. So at the end of the mesoscale modelling chain.
Linking the nowadays very popular WRF NWP mesoscale model to microscale models such as WAsP.
When you use mesoscale simulations for wind resource assessment there is an issue with the resolution
If you want to use WRF mesoscale simulations for wind resource assessment there is a problem due to the environmental representation by wRF. So, this is how WRF

## Slide 2: Introduction
Reality
Limited resolution
Area averaged topography
Simulated wind ≠ on-site measurements
Wind climate Generalisation
http://www.remotetraveler.com
Hahmann, A. N et al. (2013)
Environment by WRF
VS.
Notes: This mesoscale to microscale coupling is necessary due to the limited representation of the environment by WRF. This picture sketches the environment as seen by the WRF model, so consisting out of squares with 1 defined height and 1 area averaged roughness length. The size of each square being about 5 by 5 km.
This does of course not agree with the actual environment, which is much more complex.
This limited resolution and area averaged topography representation makes direct use of the WRF mesoscale model as a replacement for wind measurements impossible.
But as a solution we can make us eof the concept of wind climate generalisation.

## Slide 3: WRF generalisation procedure
WAsP
Generalised simulated
Wind climate
Local wind
climatology
Mesoscale
Generalisation
WRF simulated
wind
Orography model
Roughness change model
Flat + homogeneous terrain
Notes: The generalisation procedure removes the effect of the low-resolution topography representation by WRF as follows:
The WRF simulated wind is generalized by removing the effect of the mesoscale surface using a roughness change model and the effect of the mesoscale orography with an orographic model.
This results in a generalized simulated wind climate over a flat and homogeneous terrain. And is stored as wind roses and Weibull distributions. These statitistics can then be used as input for a microscale model such as WAsP to downscale and obtain the local wind climate. These microscale model reintroduce the roughness and orography effects, but now with a much higher resolution and greater detail than the original WRF map.

## Slide 4: WRF generalisation procedure
From heterogeneous to homogeneous terrain
Geostrophic drag law
Geostrophic wind
Preference for narrow bin widths
But need to be in agreement with simulation length
Too narrow bins cause large errors and generalisation procedure fails
Apply on histograms
Highly empirical
Assumes stationarity
Sensitivity study
Appropriate bin widths?
Notes: In order to go to from a heterogeneous terrain with different roughness changes to a uniform homogeneous terrain we make use of the concept of the geostrophic wind by applying the geostrophic drag law.
However, this law is highly empirical and assumes stationarity. So instead of applying it directly on the simulated time series, we are first going to bin the time series into histograms and apply the formulas onto the different histogram bins.
This then raises the question what bin sizes for wind speed and direction would be appropriate. And to find this out, I performed a sensitivity study using different bin sizes. This study showed that there is a benefit of using narrow bins for both wind speed as wind direction. However, they cannot be chosen too narrow and should be in

## Slide 5: Data
D01
D02
D03
D01
D02
D03
Same period
WRF simulations
Hourly output
YSU PBL scheme
Measurements
+ WAsP project
> 60 m + min 1 year
31 masts in France and Belgium
5 masts in Thailand
1 or 2 years
Large bin width for generalisation

## Slide 6: Validation
Simulated wind
Measurements
RAW
GENERALISED
Generalised climate
Local wind
WRF
Comparing WRF simulations with measurements
Notes: Clearly explain raw and generalised

## Slide 7: Validation
Validation criteria
At each mast:
Calculate mean wind speed error
IQR
Measure for precision
Measure for accuracy

## Slide 8: Results
IQR
nMAE
Mean wind speed error
Lower absolute error
Higher accuracy
Higher precision
Visualises absolute error, bias and spread in a single graph
Notes: Define ‘better’: Generalisation makes the result more accurate (almost on arc of 1) and precise (smaller angle with abscissa). And it also reduces the absolute error (smaller circle).
WRf simulations have a positive bias
With ‘better’ I thus mean more precise, more accurate and a lower absolute error.

## Slide 9: Results
Mean wind speed error
All
FR + BE
Thailand
17.2 %
6.5 %
15.2 %
5.4 %
Mast number
France + Belgium
nMAE
Notes: Neg underestimating, pos: overestimation
We see that WRF generally overestimates the wind speed, but that the generalization procedure is able to correct for this -> why?

## Slide 10: Results
WRF wind speed overestimation
Single value to indicate difference
WRF simulations generally overestimated the mean wind speed (over land)
Reason for this overestimation?
How is the generalisation able to correct for this?
For every mast:
Weighted difference between WRF roughness length and WAsP roughness length around mast
More detailed
Notes: WRF overestimation: what’s the reason, many other publications also report this issue of WRF wind speed overestimation over land.
I found that the WRF roughness length definition is one of the reasons for this.
For each site I calculated a weighted average of the surrounding roughness, both for WRF as Wasps map. This way I can plot the raw wind speed error of the WRF simulation as a function of this difference.
From these 36 points we can observe that there is a trend, and that there is a clear correlation between the raw WRF wind speed error and the roughness length difference between WRF and WAsP. As you would expect, WRF generally overestimates the wind speed when there is an underestimation of the roughness length compared to the WAsP roughness. You can also observe that at most sites, WRF underestimates the roughness length as compared to the detailed WAsP map, which has its effect on the overestimated wind speed by WRF.
On the other hand, we can make the same plot but using the wind speed errors when the generalization was applied. This shows that the correlation between the simulated wind speed and the WRF roughness definition by its surface model is removed by applying the WRF generalization procedure. Now we see that the red dots look randomly scattered and no correlation is visible anymore. This means that the exact definition of the surroundings by the WRF surface model does not matter anymore since the generalization removes its influence on the wind speed.
Why is it good that it’s random scatter
No effect of WRF roughness definition

## Slide 11: Results
[%]
[%]
Influence of WRF land cover is ‘removed’ by the generalisation
WRF roughness < WAsP roughness
↓
Overestimation of wind speed
RAW
GENERALISED
Random scatter
Significant correlation
Notes: WRF overestimation: what’s the reason, many other publications also report this issue of WRF wind speed overestimation over land.
I found that the WRF roughness length definition is one of the reasons for this.
For each site I calculated a weighted average of the surrounding roughness, both for WRF as WAsP map. This way I can plot the raw wind speed error of the WRF simulation as a function of this difference.
From these 36 points we can observe that there is a trend, and that there is a clear correlation between the raw WRF wind speed error and the roughness length difference between WRF and WAsP. As you would expect, WRF generally overestimates the wind speed when there is an underestimation of the roughness length compared to the WAsP roughness. You can also observe that at most sites, WRF underestimates the roughness length as compared to the detailed WAsP map, which has its effect on the overestimated wind speed by WRF.
On the other hand, we can make the same plot but using the wind speed errors when the generalization was applied. This shows that the correlation between the simulated wind speed and the WRF roughness definition by its surface model is removed by applying the WRF generalization procedure. Now we see that the red dots look randomly scattered and no correlation is visible anymore. This means that the exact definition of the surroundings by the WRF surface model does not matter anymore since the generalization removes its influence on the wind speed.
The exact mesoscale surface representation does not play any role
Why is it good that it’s random scatter
No effect of WRF roughness definition

## Slide 12: Conclusions
Overestimation ‘raw’ WRF simulations → no direct use possible WRF
WRF Generalisation corrects for WRF ‘topography difference’
  17.2 % → 6.5 %
  Appropriate bin width selection required depending on WRF simulation length
Notes: Purpose: large scale wind maps
Error is expected to decrease even further when longer simulation periods are used
State that it’s more accurate , generalization needed for wind maps since you cannot directly compared WRF mesoscale simulated wind speeds with on-site measurements.

## Slide 13: Get in touch for more information!
Brussels
Paris
London
Toulouse
Milan
Istanbul
Cape Town
www.3E.eu