## Slide 1: Storm Britta
Xiaoli Guo Larsén (xgal@dtu.dk)
Jianting Du (jitd@dtu.dk)

## Slide 2: Storm Britta: context
Key deliverables of X-WiWa:
A modelling system
Extreme wind map
Extreme wave map
The X-WiWa Project: EXtreme Winds and Waves for Offshore Turbines – Coupling atmospheric and wave modelling for design and operation in coastal zones

## Slide 3: Storm Britta: context
Challenges in modeling storm winds and waves
Storm postion, path, size, intensity and spatial distribution of wind field
Accurate wind input important for wave modeling
Wave modeling is missing the peak

## Slide 4: Storm Britta: context |Characteristics
Facts from the literatures:
Brusch et al. 2008
Hs about 10 m at FINO 1 (20-year value)
Max wave height 18 m at FINO 1
Strong winds in Quikscat data
Presence of open cells
HIRHAM modeling (7 km) did not reproduce open cells

## Slide 5: Storm Britta: context |Characteristics
Facts from the literatures:
Brusch et al. 2008
Behens and Günther 2009
DWD and WAM captured Hs quite well at FINO 1
Britta and Kyrill: different paths, different strength
Open cells not modeled, not mentioned
Britta
Kyrill

## Slide 6: Storm Britta: context |Characteristics
Facts from the literatures:
Brusch et al. 2008
Behens and Günther 2009
Emeis and Türk 2009
Measurements at FINO 1
Britta and Erwin:
  Unstable and stable
  Similar wind strength, much larger Hs at Britta
Britta
Erwin

## Slide 7: Storm Britta: context |Characteristics
Facts from the literatures:
Brusch et al. 2008
Behens and Günther 2009
Emeis and Türk 2009
Pleskachevsky et al. 2012
Storm-in-storm structure updated in wind field
Spectral wave modeling, 1 km
”open cell wind” leads to increase of 6 m in Hs

## Slide 8: Storm Britta: context |Research Topic
*Is stability the cause to the extreme wave at FINO 1?
*Is open-cell the cause to the extreme wave at FINO 1?
*What is the mechanism behind that caused the extreme wave at FINO 1?

## Slide 9: Findings
Not stability directly…
Not open cells…
It is the intensive cold front with a special path…

## Slide 10: Method
Combination of various types of measurements, reanalysis data and mesoscale numerical modeling
Use COAWST modeling system (WRF+SWAN)
Analysis of groups of storms of different conditions (stability, open cells, storm path, storm intensity)

## Slide 11: Measurements

## Slide 12: Modeling system
WRF:
CFSR + SST
46 vertical sigma levels
MYNN 3.0 PBL scheme
Thompson microphysics scheme
RRTM long and short wave radiation
Kain-Fritsch cumulus scheme (I, not II & III)
Corine land use
SWAN:
1/8 arc-minute bathymetry data
Initiated with JONSWAP spectrum
Outer domain open boundaries with JONSWAP spectrum with Hs = 0.5 m, Tp=1 s
36 directional bins, resolution of 0.1 f and 0.03 Hz < f < 1.02 Hz.
Komen input and dissipation source func.
2-way online
Nested: 18 – 6 – 2 km
2006-10-30 to 2006-11-02
36 hours for each run
I
II
III
WRF
SWAN
U10 ,V10
z0 (Tp)

## Slide 13: Results
T2m – SST (K)
2006-10-31 16:00
2006-11-01 04:00
Temperatures at FINO 1

## Slide 14: Results
U at 10 m (m/s)
U at 100 m at FINO 1
4:00 1st Nov
10:00
13:00
22:00

## Slide 15: Results
Hs (m)
4:00 1st Nov
10:00
13:00
22:00
Hs at FINO 1

## Slide 16: Results
Open cell
Høvsøre, 80 m
Horns Rev II, 107 m
Kaimal
obs
Open cell issues
4:00 Sin
10:00 Sds
4*10-5
2*10-5
0.02
0.02
13:00 Snl
22:00 Stot=Sin-Sds+Snl
4:00
10:00
13:00
22:00
Hs (m)
Notes: S_tot ~change of the spectrum -> change in Hs

## Slide 17: Results
Storms examined
  Behrens and Günther’s list
  10 storms from 2006 to 2013 identified at FINO 1 (U33 > 10 m/s, Hs>6 m): 2006 to 2013
Conditions examined
  Spatial distribution of wind and wave vectors during the storm
  Atmospheric stability
  Presence or absence of cells
  Presence or absence of extreme waves
Britta
MSLP 20061031 16:00
Longitude

## Slide 18: Summary and applications
COAWST is capable of capturing main characteristics of storms like Britta for open seas
The development of extreme wave at FINO 1 benefits from the persistent strong wind field with a long undisturbed fetch over a long period.
Unstable stratification and open cells are two phenomena that alone are not responsible for the generation of extreme waves
Hundreds of storms, responsible for extreme wind and wave climate for water areas around Denmark, have been identified and will be modelled using COAWST, for further calculation of the 50-year return values.

## Slide 19
Acknowledgements:
Supported by Danish ForskEL PSO 12020 XWiWa project.
Thanks to our colleagues from DTU Wind Eenergy and DHI.
Thanks to FINO 1, DONG Energy and Vattenfall for Horns Rev data, European Space Agency for the SAR data, NERC Satellite Recieving Station, Dundee University for the cloud pictures, UCAR for CFSR data.
Thank you for your attention!