## Slide 1: The model chain and the full scale horizontal wind spectrum of the boundary layer wind EL Petersen, XG Larsén, SE Larsen DTU Wind Energy, Risø Campus
Extensive mean meteorological data and high frequency sonic data from 3 sites, two coastal onshore and one offshore, have been used to study the full scale spectrum of the boundary layer wind, over frequencies from 1 year-¹ to 10 Hz and heights from 10m to 241m
Notes: It is only in the presentation I appear first – suggestion from Xiaoli. Too much text?

## Slide 2: Why is it interesting to study the spectrum for the Model Chain?
The understanding of the physics of the spectral behaviours at different scales and the scale separation can guide us in building the models constituting the Model Chain.
A very important aspect of the full scale spectrum is the (possible) existence of a spectral gap between the 2D and the 3D atmospheric motions.
The spectral gap is essential for obtaining turbulence quantities through measurements and for the their use in the microscale models and the parameterization of the subscale processes in the mesoscale models.
The spectral gap ensures that measured turbulence (can) fulfils the criteria of ergodicity and stationarity.
Notes: (Needs editing)

## Slide 3
In recent paper published in Boundary Layer Meteorology - we present:
1) summary of the history of the “Gap and its importance”
2) New analyses being made possible by new data and analysis technology
3) New models for the characteristics of the gap, validated by the data. These new models are shown in this presentation.
Notes: (Needs editing?)

## Slide 4
NEW EUROPEAN WIND ATLAS
Verification & Validation
Orography
Topography
Land use & roughness
Cities & environment
DATABASE
Input for models and experiments
Reanalysis data
Meso scale
Micro scale
MODEL CHAIN
- Complex terrain
Forest
Offshore
Coastal
Wakes
Exp . Database
Deliverables in the new European Wind Atlas
EXPERIMENTS
Model interface
- Open platform
Model runs
Models of uncertainty
Wind data & Design Param.
Speedup, Extremes, Turbulence, Icing conditions, Offshore waves, etc.

## Slide 5
The figure shows the grids size, Δ, for meso scale and LES models relative to the turbulence spectrum, according to (Wyngaard, 2004)
TERRA INCOGNITA (the nightmare of model chain modelers)
Notes: Illustration of the Model Chain problem

## Slide 6
fS(f)
f
Van der Hoven spectrum
Wishful thinking but fundamental to classical atmospheric turbulence theory (M-O scaling)
Notes: The classical “wishful thinking” illustration of the large scale – turbulence scale separation and non-correlation.

## Slide 7
Measurements: Østerild, Høvsøre and Horns Rev
Østerild
Høvsøre
Horns Rev
“Land”
Coast
Offshore
Notes: Location of the 3 sites. Perhaps we could make one figure with a map showing all 3 sites and the Østerild mast. The other two sites are depicted in the first slide.

## Slide 8
Spectral behaviours:
Variation with height and geographical location of the full scale boundary layer horizontal wind spectrum and the spectral gap between meso scale and micro scale

## Slide 9
f S(f) m2s-2
f Hz
Horns Rev
Spectra of wind speed at 45 m at Horns Rev, from 1 year 10-min mean values and from day-long 20 and 12 HZ time series
45 m
Notes: Central to this study – and for the first time – the full scale spectrum of the boundary layer horizontal wind from 7m to 241m. The apparent disappearance of the spectral gap is clearly shown as is the existence of the daily variation at all heights. (Does the figure needs some editing?)

## Slide 10
f S(f) m2s-2
f Hz
Høvsøre
Spectra of wind speed at 3 heights at Høvsøre, from 1 year 10-min mean values and from day-long 20 HZ time series
10 m
100 m
80 m
Notes: Central to this study – and for the first time – the full scale spectrum of the boundary layer horizontal wind from 7m to 241m. The apparent disappearance of the spectral gap is clearly shown as is the existence of the daily variation at all heights. (Does the figure needs some editing?)

## Slide 11
f S(f) m2s-2
f Hz
241 m
175 m
103 m
37 m
7 m
Østerild
Spectra of wind speed at 5 heights at Østerild, from 1 year 10-min mean values and from day-long 20 HZ time series
Notes: Central to this study – and for the first time – the full scale spectrum of the boundary layer horizontal wind from 7m to 241m. The apparent disappearance of the spectral gap is clearly shown as is the existence of the daily variation at all heights. (Does the figure needs some editing?)

## Slide 12
Total horizontal wind spectrum at 10 m, composed by the extrapolation of the low frequency form and a Kaimal- shape fitted to the peak for the ABL spectrum.
Simple Genesis model for Total Wind Spectrum in Gap region, z=10m
Høvsøre
Eq.1 :
Notes: (The low frequency form 0.7*Eq 1 not explained)

## Slide 13
Simple Genesis model for Total Wind Spectrum for z = 80, 100m
Total Horizontal wind spectrum at 80 m, composed by the extrapolation of the low frequency form and a Kaimal- shape fitted to the peak for the ABL spectrum.
Høvsøre
Eq.1 :
Notes: Showing how the gap can be retrieved by means of the model.

## Slide 14
Østerild
241 m
175 m
37 m

## Slide 15
Spectral behaviours:
Diurnal Peak
The daily variation of the wind changes with height and is a strong stability measure. The spectral component S(f)|f=1 day-1 is studied in the next figures

## Slide 16: (a) Spectra of wind speed at 5 heights at Østerild, from 1 year 10-min sonic data time series (dashed curves) and from day-long 20 Hz sonic time series (solid curves). Note 7 m is most likely sheltered by a surrounding forest.
Østerild
a
b
c
(b) Spectra of wind speed at 6 heights at Høvsøre
(c) Spectra of wind speed at 4 heights at Horns Rev
Points at 1/day
Notes: Same as previous figure with all spectra on top of each other.

## Slide 17: Variation of S(f)|f=1 day-1( the daily cycle of the wind speed) with height.
Østerild
Høvsøre
Horns Rev
m
250
200
150
100
50
0
Height
S(f)|f=1 day-1
Notes: The variation of the daily cycle with height is a strong indicator of stability variations with height. The minimum at around 100m is at the same height where the Wiebull k-profile often is found the show a maximum indicating minimum variance. An important guiding measure for modellers.

## Slide 18
Conclusion.
One of the intentions of our analysis has been to aid the work with the New European Wind Atlas with regard to:
Building the Model Chain. The analysis of the full scale horizontal wind speed spectrum and the spectral gap it should be useful for the work with resolution issues and closure developments for the numerical models.
The measurement campaigns. The structure around the gap may be used for specifying the necessary (natural) time windows for measuring turbulence characteristics.
Specific results
The full spectrum can be considered a linear composite of PBL turbulence and ”mesoscale “, 3D and 2D
The Gap is clearly present at lower heights and at heights where it is almost non-visible it can be recovered assuming that the meso scale and the PBL turbulence is uncorrelated.