## Slide 1: The use of Smart Drones in Wind Energy
Lars Landberg1, Elizabeth Traiger1, Kevin Lind2, Kostas Karachalios2, Chris Day2, Thomas Richardson3
1DNV GL, SR&I/GTR, Renewables, UK & Denmark
2Perceptual Robotics, UK
3Bristol University, UK

## Slide 2: How the three organisations work together
DNV GL: certification and advisory. Need to understand latest technology > give advice, formulate practices
University of Bristol: need to research and develop the latest technologies
Perceptual Robotics: UoB spin out, to commercialise research.
Smart drones

## Slide 3: Contents
The hardware
Smart Drones
  Autonomy
  Deep learning for image recognition
  Economy
  Perspectives
Robots: dull, dangerous, dirty

## Slide 4: UAV Platforms
DJI Phantom 3
Dhalion Test Platform
Key criteria to automation
Dynamic path optimisation
Multilayer safety technologies
Time efficient, robust, repeatable inspections
Dhalion Full Platform
1 Pixel/cm2
100 Pixel/cm2

## Slide 5: Smart drones
Autonomous flight (video!)
AI used for image processing (example)

## Slide 6: How the smart drone works
At the press of a button the drone, utilizing local sensing and intelligent pathing, flies a path around the turbine.
During flight images are taken of the entire exterior of the turbine.
The data is processed to identify faults, and produce a report outlining the results.

## Slide 7: How the smart drone works
Low Resolution Camera- Captures images for localization, mapping and obstacle avoidance
15 FPS
640x380 pixels
2D Lidar- Takes distance measurements for localization, mapping and obstacle avoidance
Range:30m+-1cm
270 degree FOV
High Level Processor- Fuses sensor data, updates flight path
8-core, 2.5 GHz
Low Level Autopilot- Stabilise Flight
4-core, 180 MHz processor
failsafe co-processor
3-axis gyroscope
3-axis accelerometer / magnetometer
3-axis accelerometer/gyroscope
Barometer
GPS
Main Camera- Captures inspection data
8000x4500 pixels
High Performance UAV
Dhalion Software System

## Slide 8: Video: Actual inspection of wind turbine (Autonomous!)

## Slide 9: Automated Image Processing
Drone Captured Image
Image Pre-processing enhancement, smoothing, denoising, subsampling
Segmentation ROI & background
Feature Extraction shape, texture, LTE, Tamura, wavelet ...
Probabistic Classification
Classification Algorithm SVM, random forest, k-NN, NN …
Decision Defect / Pass
Dimension Reduction
Notes: Image Pre-processing
Image pre-processing can be applied to reduce the computational cost through multi-scale image decomposition such as subsampling or wavelet transform. Then the low resolution images obtained this way can be first analysed to roughly locate the regions of interest [ROI], and only these regions go to the higher resolution processing step. In case of poor quality image input, e.g. severe noise, low intensity contrast with weak edges, and intensity inhomogeneity, other pre-processing techniques such as image smoothing, de-noising, and enhancement may be applied for image restoration
Segmentation
Image segmentation extracts objects/regions of interest from the background; these objects and regions are the focus for further identification and classification. Segmentation methods include thresholding, edge detection, region growing, clustering.
Feature Extraction
After image segmentation, image features are extracted from the regions of interest to detect potential defects. Algorithms exploit characteristics unique to defects as apposed to manufactured features with respect to object size and shape (e.g. compactness and regularities), topological or graph-based features (e.g. Voronoi diagrams, Delaunay triangulation, and minimum spanning trees), intensity and colour features (e.g. statistics in different colour spaces), and texture features (e.g. Haralick entropy, Gabor filter, power spectrum, co-occurrence matrices, and wavelets). In addition, to the spatial domain, many features can also be extracted from other transformed spaces, e.g. frequency (Fourier) domain and wavelet transforms.
Dimension Reduction
With multiple classes of features extracted from large size images, the resulting vast quantity of data (e.g. a feature vector with thousands of elements for each pixel) can be prohibitive for feasible analysis, even with current high performance computing machines. Feature selection or dimensionality reduction schemes are necessary to determine the most discriminative features. Direct feature selection is generally inefficient and suboptimal due to the large amount of features. Linear techniques, such as principal component analysis (PCA) linear discriminant analysis (LDA), and multidimensional scaling (MDS) are used in cases of linearly separable points in the feature space.
Classification Algorithm
The final defect feature class is then run through a machine learning algorithm. Supervised algorithms, where a training set of labelled inspection images have been provided, can be applied to build the classifier. These include artificial neural networks, boosting approaches (e.g. AdaBoost), support vector machine (SVM), and decision trees. In addition, Bayesian model­ based approaches such as Markov random field (MRF) hidden Markov model and conditional random field (CRF) are commonly used in medical diagnosis. Without a set of labeled images, unsupervised techniques, such as K-­means, self ­organizing maps and deep learning algorithims can be used to flag anomalous features.
Probabilistic Classification
Depending on the algorithm chosen, the classification can have a probability of class assignment. Probability thresholds can be set for final classification.
Decision Defect / Pass
A final decision is made, defect locations are added to an O&M databases and report generated.

## Slide 10: Segmentation

## Slide 11: Defect Feature Processing and Identification
Notes: Original Image

## Slide 12: Economics
Still early days…
An example could be:
A 100-wind turbine wind farm
Complete inspection required
Manual inspection: two people per turbine for around a day  200 person days
A drone can inspect one turbine in no more than an hour  100 drone hours
The drone might identify 15 turbines that need manual inspection 30 person days

## Slide 13: “Future” applications
BVLoS
Autonomous flight: “just bring your drone in a box” 
AI to “look at” footage, identifying critical areas, and turbines to be inspected 
IR cameras 
Documentation 
Long term and more frequent inspection  Analysis and preventive maintenance
VR: remote control of drone
AR: goggles let you see details and wavelengths you cant normally see

## Slide 14: Summary
The hardware
Smart Drones
Autonomy
Deep learning for image recognition
Economy
Perspectives

## Slide 15: Thank you!
Contact
Lars.landberg@dnvgl.com
+45 50 58 55 24