## Slide 1: Validation of CFD based forest modeling for large forested areas with many measurement masts
Gibson Kersting E.ON Climate & Renewables, United States ,
Catherine Meissner, Matteo Mana, WindSim AS, Norway

## Slide 2: Outline
  Introduction
  Forest maps
  CFD forest models
  Validations
  Atmospheric stability
  Conclusion
Notes: First, I’ll give a brief introduction on why we decided to do this work.
Second, I’ll talk about the forest maps and how they have been created.
Third, I’ll talk a little bit about CFD forest models
Fourth, I’ll present the validations that we did for 2 projects with several met masts.
Fifth, I’ll talk about atmospheric stability and why it is important when using CFD.
Lastly, I’ll just give a brief conclusion of our findings.

## Slide 3: Introduction
  Forested sites in complex terrain represent a great challenge for development of wind farms.
  Using multiple met masts to reduce wind flow model uncertainty.
  Using WindSim CFD code with forest model and high resolution GIS data is a great opportunity to test the impact of different forest parameters in complex terrain.
8.5 km wide
13 km long
9 met masts (all higher than 80m equipped with class I sensors)
Example
Notes:   Forested sites in complex terrain represent a great challenge for development of wind farms.
  That is why people install or should install several met masts to reduce wind flow model uncertainty and that is what we did.
  So Using WindSim CFD code with forest model and high resolution GIS data is a great opportunity to test the impact of different forest parameters in complex terrain.

## Slide 4: Forest maps
~ 2.3 million trees above 2m
~ 52 square kilometers
~ 1 tree for every 22 square meters
Example
High Resolution Data
Notes: Here is one of our forest maps.
I’ve split the forest map in 3 regions because this is how the forest map is actually set up.
First, we have a high resolution forest map within the project footprint. You see from this image that we got a tree map with a laser scan that captured the height of every single tree on side.
On this second plot you can see the distribution of trees on that high resolution area and you can see that it has a Weibull shape. On this case I’ve only considered trees higher than 2m.
2.3 million trees above 2m
~ 52 square kilometers
~ 1 tree for every 22 square meters (here we have some clearings on site. In fact 8% of what you see are clearings so we’re talking about 1 tree for every 20 square meters).

## Slide 5: Forest maps
Mid resolution data
Data surveyed by the forest manager.
Average tree height and species in each polygon
Tree type
CORINE Land Cover
Low resolution data
Notes: Next, we have what we call the mid resolution data.
  This data was surveyed by the forest manager where we develop the project.
  Each one of the polygons that you see here have the average tree height, species as well as the tree type.
  Lastly, we have the low resolution data that is just CORINE data. Here we set the tree height for the CORINE data as the average tree height of the high resolution data since we believed that the development area was a very good sample of the region.

## Slide 6: CFD forest models
  Influence of the forest on the turbulence equations and calculation of parameters
Formally the model has been implemented as in Sanz (2003) and Katul (2004) with the model constants revised to be compatible with the default set of constants of the standard k-ε model.
TKE
Dissipation rate
Source and sink in TKE
Source and sink in
Parametrization
Forest information
Momentum
Momentum sink high Re
Notes: Let’s now turn our attention to the CFD forest model that we’re using.
First, we have the momentum equation. So the Navier-Stokes equations in steady and incompressible form including a momentum sink term.
Here we have our momentum sink term. For high Reynolds numbers the viscous drag is much smaller than the pressure drag. A model validation by Cai in 2011 confirmed that.
Next we have our turbulence kinetic energy coming from the k epsilon model including the source and sink term due to forest.
Then we have our dissipation rate equation for the k epsilon model including the source and sink term due to forest.
Next, we have our source and sink term in turbulent kinetic energy and now the same on dissipation rate.
And here we have the parametrization for the equations above for the k-epsilon model.
Lastly, we have our C2 which is dependent upon the leaf area index, the height of the canopy and the thrust coefficient for the trees.
Formally the model has been implemented as in Sanz (2003) and Katul (2004) with the model constants revised to be compatible with the default set of constants of the standard k-ε model
It is important to stress that such model has been selected by WindSim based in a master thesis by David Hilbert in 2011 where several forest models were addressed and this one was found to be the best fit for WindSim.

## Slide 7: Validation Site I
8.5 km wide
13 km long
9 met masts (all at least 80m high equipped with class I sensors)
Notes: - Let’s now turn our attention to the validation part of the work. More specifically to the validation site I.
- The site is in a complex terrain environment and it is 8.5km wide and 13km long. We have 9 met masts installed all with class I sensors.
The forest on this project is mostly uniform. That means not many clearings. However, the area where we have substantial clearings can be seen on this picture.
As I said most of the forest is uniform without many clearings as on this picture.
Some areas are a little bit more challenging with really high trees (about 20m) next to 5m trees as on this portion right here.

## Slide 8: Validation Site I
Displacement height only
Forest model C2 = 0.5
Forest model C2 = 0.05
Forest model C2 = 0.1
Notes: We have modeled the sites with different forest parameters. We haven’t included all on this presentation.
Let’s take a look on the shear profiles.
First, we used displacement height only and no forest model. We don’t have the information here but we did that using just CORINE data and we got very similar results, meaning that more accurate forest data without a forest model doesn’t do a good job.
Second, we tried the forest model with different C2s. Remember that C2 is dependent upon height, leaf area index, and thrust coefficient. We actually calculated the C2 for the site and we found to be 0.13; however, as you see C2 = 0.05 fit the model the best.

## Slide 9: Validation Site I
Cross Prediction results neutral simulation C2= 0.05 for all forest types
Met Mast 9 seems to be not well described by the CFD model
Forest parameter | Average absolute error [%]
C2 = 0.05 | 4.51
C2 = 0.1 | 5.56
C2 = 0.5 | 5.75
Displacement Height | 5.51
Notes: Here we have the cross-prediction results for all masts on site. We see that C2 = 0.05 was the best one. It is interesting also, the displacement height did as well as the forest model. My recommendation is that if you can calculate C2 but always try to run with different constants around the calculated value in order to tune the model.
Also, you can see that mast 9 is not being captured well by the model. We saw no indication that this was related to the forest model but actually by the speed up factors in 5 sectors that were consistently over predicting which caused such large absolute errors. This sends a strong message. The absolute error for the project without mast 9 would have been 3.1%. That reinforces the argument to install additional masts in forested and complex sites.

## Slide 10: Validation Site II
13 km wide
21 km long
6 met masts (at least 100m high equipped with class I sensors) and 1 LiDAR
Notes: Now let’s turn our attention to site II. This is a bigger site than the previous one.
This is 13 km wide
And 21 km long
We have 6 met masts at least 100m high equipped with class I sensors and 1 LiDAR.
You can see that the masts are in some challenging areas.
The forest here is also much more complex than the previous site. This forest has some really dense areas like on this picture but clearings are everywhere.
Also, there are areas with very low tree density surrounded by lakes like on this picture.
On this zoomed area you can see the magnitude of the problem. Several patches of forest that are more than 20m high surrounded by a lot of clearings and some lakes.

## Slide 11: Validation Site II
Displacement height only
Forest model C2 = 0.5
Forest model C2 = 0.05
Forest model C2 = 0.1
Notes: Here we have the profiles.
Here we see that C2 = 0.5 performed better. This forest is quite different from the previous one. The difference in the average tree height is only 1m but the number of tall trees is much higher on site 2 resulting in a higher leaf area index.

## Slide 12: Validation Site II
Cross Prediction results neutral simulation C2= 0.5 for all forest types
Met Mast 3 seems to be not well described by the CFD model
Forest parameter | Average absolute error [%]
C2 = 0.05 | 9.20
C2 = 0.1 | 9.46
C2 = 0.5 | 4.39
Displacement Height | 4.93
Notes: Here C2 =0.5 did the best based on the characteristics of the forest.
Also, we had one mast that didn’t perform well on this situation and we also believe it is not related to the forest. We have the same problem of consistently over-predicting in some of the sectors. Once again I’d like to stress that without mast 3 the average absolute error would have been 1.8%. This once again shows how important is to have a solid met mast campaign.

## Slide 13: Atmospheric stability
  Why does it matter and how we obtain good information?
  Some sectors do not have in average neutral conditions
  In cold areas often the measurement devices have longer downtime and therefore the wind rose of the atmospheric stability conditions from measurements is misleading
  High resolution mesoscale modeling based on reanalysis data can overcome this problem
Notes:   - Why does it matter and how we obtain good information?
  - Some sectors do not have in average neutral conditions
  - In cold areas often the measurement devices have longer downtime and therefore the wind rose of the atmospheric stability conditions from measurements is misleading
  - High resolution mesoscale modeling based on reanalysis data can overcome this problem

## Slide 14: Validation Site II
  Validation with Lidar on November and December 2015
      Stable simulations represent much better the shear and the profile is improved at hights higher than 160 meter.
Red – Stable Frequency
Blue – Neutral Frequency
Notes: - Let’s turn our attention to site II in which we had a LiDAR.
We did a validation with the LiDAR on November and December 2015.
      Stable simulations represent much better the shear and the profile is improved at hights higher than 160 meter.

## Slide 15: Validation Site II
  Validation with Lidar on November and December 2015
      Stable simulations represent much better the shear and the profile is improved at hights higher than 160 meter.
Neutral
Stable
Notes: These were the profiles for 2 directional sectors for the neutral case.
These were the profiles for 2 directional sector for the stable case. As you can see a good improvement on both cases.

## Slide 16: Conclusions
  Good vegetation data reduces errors both on the speed up factors and shear profile.
  Careful forest modelling around the met masts is key for a successful CFD run.
  Atmospheric stability information from mesoscale models improves shear profiles.
Notes:   - Good vegetation data reduces errors both on the speed up factors and shear profile.
  - Careful forest modelling around the met masts is key for a successful CFD run.
  Atmospheric stability information from mesoscale models improves shear profiles.