## Slide 1: Aerial LIDAR scans for validation of CFD models in complex forested terrain
Ebba Dellwik, Johan Arnqvist, Dalibor Cavar, Peter Enevoldsen
Paul van der Laan

## Slide 2: Motivation
12 km
In order to validate our models for this site, we need
consistent high-quality land surface information over
large areas.

## Slide 3: Outline
Introduction: Forest parameterization for wind modeling
Method: Forest (and surface) parameterization tailored for CFD flow models based on aerial lidar scans.
Method: CFD solver
Validation and conclusion

## Slide 4: Forest parameterizations for wind modeling
Displacement height and surface roughness for roughness models.
- Defined via wind measurements
Distributed drag force for CFD models.
~Forest structure, height and density.
Tree height
PAD ~
shape of tree
PAI ~
vertically integrated PAD

## Slide 5: Main idea: use observations about forest structure and avoid tunable parameters in the land surface description
John von Neumann
(December 28th 1903 – February 8th 1957)
“With four parameters I can fit an elephant, and with five I can make him wiggle his trunk”

## Slide 6: How: Use aerial lidar scans to characterize all parameters needed for land surface modeling.
The (x,y,z) coordinates of the lidar reflections form a point cloud.
The point cloud reflections carry information on the land surface: its level, ruggedness and vegetation cover.
Point cloud data are increasingly available.

## Slide 7: How? Extend and develop on previous work for forest parametrization*
PointCloud Postprocessor
”PC-Post”
* Boudreault et al. (2015): A lidar method for canopy structure retrieval Agricultural and Forest Meteorology 201, pages: 86-97
Orography grid
Forest structure grid
Grid of water areas/land cover
Surface roughness for areas with no vegetation.
Quality control parameter

## Slide 8: Outputs from PointCloud-PostProcessor ~1.5 billion points, ~10 min on cluster: terrain (m)

## Slide 9: Outputs from PointCloud-PostProcessor ~1.5 billion points, ~10 min on cluster: tree height (m)

## Slide 10: Outputs from PointCloud-PostProcessor ~1.5 billion points, ~10 min on cluster: PAI m2/m2
PAD

## Slide 11: Outputs from PointCloud-PostProcessor ~1.5 billion points, ~10 min on cluster: ground roughness proxy (m)

## Slide 12: Outputs from PointCloud-PostProcessor ~1.5 billion points, ~10 min on cluster: water areas

## Slide 13: CFD model setup description
EllipSys 3D* Inner square grid 14 km x 14 km
Outer circular grid r = 20 km Domain height: 10 km
Resolution:
Inner grid: 20m Outer grid: 64 points from r = 7km to r = 20km.
Inlet profile: SCADIS 1D, with Ug = 15m/s, 10 m/s
Length scale limiter: Blackadar type
Buoyancy/temperature effects not included
Inner grid
Outer grid
*
U

## Slide 14: First check: Inner domain 100 m wind speed (m/s)
Case with no forest
constant z0 = 0.5m
Case with forest
output from PC-Post

## Slide 15: First check: Inner domain 100 m wind speed (m/s)

## Slide 16: Selection of data to match model capacity for neutral atmosphere
No information on stability from towers 1-7
From reference site, instrumented with sonic anemometers
All data
Near-neutral

## Slide 17: Validation 270: wind speed all data normalized on Tower 1, 60m
U
Notes: We predict more difference than is observed.

## Slide 18: Validation 270 : turbulence intensity

## Slide 19: Conclusions
Thanks for listening!
Aerial lidar scans were used as basis for an automated forest and land surface parameterization, tailored for CFD applications.
When adding the forest parameterization, the turbulence intensity predictions improved.
… but the ability to cross-predict the mean wind speed between different towers was not generally improved.
ebde@dtu.dk
Attendance at DTU stand, 574, Hall B6, 16:00-18:00 today.

## Slide 20: DTU Wind Energy at WindEurope Summit 2016: Stand 574, Hall B6