## Slide 1
WindEurope Summit 2016, Hamburg
Wind flow modelling uncertainties in forested terrain
Claude Abiven and Elie Gournay

## Slide 2: Outline
Trees add a level of complexity to wind flow modelling
To which extent do modelling choices affect yield?
  Input data
  Forest modelling
What is the error we can expect from different methodologies?
  Vertical extrapolation
  Horizontal extrapolation

## Slide 3: Input data – methodology for sensitivity calculation
Model sensitivity
Two sites
Base case
  VENTOS CFD model
  5 and 10m resolution topography
  Roughness from LIDAR survey
  No canopy model
Change one parameter at a time
  Compute yield

## Slide 4: Input data – site 1
Model sensitivity
global data
site visit and available maps
satellite data
LIDAR survey
  25 turbines
  In the vicinity of trees
  1% RIX

## Slide 5: Input data – site 2
Model sensitivity
global data
site visit and available maps
satellite data
LIDAR survey
  11 turbines
  In the vicinity of/within trees
  3% RIX

## Slide 6: Sensitivity to input data
Model sensitivity
Chart: Sensitivity on yield
| roughness - satellite | roughness - handmade survey | roughness - global data | topography - srtm
Site2 | 0.001532 | 0.0038976 | 0.012532 | 0.020658
Site1 | 0.0037933 | 0.00054132 | 0.0053923 | 0.0044629

## Slide 7: Forest modelling – roughness model
Roughness model
  No ZPD
  Lower hub height using ZPD
    ZPD GLGH (2)
    …
Model sensitivity
    ZPD =
    ZPD GLGH
Stull R. B. 1988
Corbett J.-F. and Landberg L. Optimising the parameterisation of forests for WAsP wind speed calculations: a retrospective empirical study

## Slide 8: Forest modelling – canopy model
CFD canopy models
  Additional terms in RANS equations
    Drag in momentum equations
    Production and dissipation terms in turbulence equations
  4 parameters terms. Several parameterizations exist
    Lopes da Costa (3)
    Svensson Häggkvist (4)
    …
Model sensitivity
(3) Lopes da Costa J.C. 2007. Atmospheric flow over forested and non-forested complex terrain. Universidade do Porto
(4) Svensson U. and Häggkvist. 1990. A two-equation turbulence model for canopy flows. Journal of Wind Engineering and Industrial Aerodynamics

## Slide 9: Sensitivity to model parameters
Model sensitivity
Chart: Sensitivity on yield
| mesh - lower resolution | canopy - Svensson Häggkvist | ZPD - 2H/3 | canopy - da Costa | ZPD - GLGH | model - linear
Site2 | 0.0013136 | 0.001532 | 0.0085436 | 0.0038976 | 0.010018 | 0.023472
Site1 | 0.00072399 | 0.0067374 | 0 | 0.0097294 | 0.0031096 | 0.0095851

## Slide 10: Error on vertical extrapolation – methodology
Use masts with cups at 3 heights (h1, h2, h3) with concurrent data
  17 masts
Use shear α from 2 lower cups to extrapolate from middle to top cup
  Assuming shear does not vary with height
  Adapting measurements with zpd
  Adapting measured shear α with modelled shear ß
Compare predictions to measurements at top
Vertical extrapolation
(5) Brower M. 2012. Wind resource assessment. Wiley & Sons, Inc.

## Slide 11: Error on vertical extrapolation
Vertical extrapolation
Chart: Mean of absolute errors on wind speed
| CFD canopy | ZPD GLGH | CFD roughness | ZPD 2H/3 | Measurements
 | 0.018582 | 0.020535 | 0.021389 | 0.023307 | 0.023893
Error bars show uncertainty on measurements mean

## Slide 12: Horizontal extrapolation – methodology
Use mast pairs with concurrent data
  26 mast pairs
  12 mast pairs with ΔZPD > 3m
Run models
  Linear
  CFD
  CFD + canopy model
  CFD + ZPDs
Use mast 1 + model to predict mast 2
Compare predictions to measurements at mast 2
Horizontal extrapolation
Chart: GLGH ZPD [m]
| 0 | 3 | 6 | 9 | 12
 | 12 | 9 | 12 | 14 | 5
Chart: GLGH ΔZPD [m]
| 0 | 3 | 6 | 9 | 12
 | 14 | 5 | 5 | 1 | 1

## Slide 13: Error on horizontal wind speed extrapolation – all data
Horizontal extrapolation
CFD roughness
adjusted with ZPD
Caveat: 14 mast pairs with ΔZPD = 0
Chart: Mean of absolute errors on mean wind speed
| CFD roughness | CFD ZPD 2H/3 | CFD ZPD GLGH | CFD canopy | Linear
 | 0.038855 | 0.039087 | 0.039324 | 0.04168 | 0.050408

## Slide 14: Error on horizontal wind speed extrapolation – ΔZPD > 3m
Horizontal extrapolation
Caveat: only 12 mast pairs left with ΔZPD > 3m
Chart: Mean of absolute errors on mean wind speed
| CFD roughness | CFD ZPD 2H/3 | CFD ZPD GLGH | CFD canopy | Linear
 | 0.038853 | 0.040883 | 0.040717 | 0.036748 | 0.044167
CFD roughness
adjusted with ZPD

## Slide 15: Conclusions
Wind flow modelling uncertainties in forested terrain
To which extent do modelling choices affect yield?
  Roughness map can impact the P50 to similar levels as topography in forested terrain
  Choice of roughness/canopy model/ZPD can impact the P50 to similar levels
What is the error we can expect from different methodologies?
  Vertical extrapolation
    Correcting measurements is beneficial
    CFD + canopy correction seems best
  Horizontal extrapolation
    ZPD does not seem beneficial to CFD
    CFD (no canopy) is a safe choice
    Canopy model beneficial within non-homogeneous forests ?