## Slide 1: Approach to wind wave correlation in coupled analysis of offshore WTG substructures
WindEurope Summit 2016
29th September, Hamburg
Trevor Hodgson
Dr Narasimhan Sampathkumar
Irina Cortizo

## Slide 2: Outline
    Introduction
    Analysis Requirements
    Different approaches to Wind Wave correlation
    Atkins Wind Wave correlation methodology
    Best Fit analysis - results
    Conclusions
    Q&A

## Slide 3: Introduction
Offshore wind turbines need to be designed to withstand wind and wave environmental conditions throughout their design life (typically 25 years)
Because of the dynamic response, one of the requirements of an efficient design process is to simulate the complete system including the tower and foundation for strength and fatigue conditions
Current practice is to perform analysis using time domain procedures, which can be very computationally intensive and lengthy
At any given site, wind and waves are intricately related to each other in terms of their magnitude, directions and even the percentage of occurrences over 1,5,10 and 50yr return periods
Establishing a realistic correlation between the wind and wave conditions is hence a pre-requisite for any type of coupled analysis process between the wind turbine and the sub structure

## Slide 4: Data Complexity
For fatigue design, a large number of wind-wave combinations exists and some simplification of these is necessary to reduce total analysis times to practical levels
Wind speed at Hub (Vh) vs Significant wave height (Hs)
Significant wave height (Hs) vs Zero Crossing period (Tz)
Site specific Wave rose
Site specific Wind rose

## Slide 5: Different Approaches to Wind Wave Correlation
match probabilities
Approach 1: Analyse all possible combinations | Approach 2: Correlate the wind condition to the sea state that has the same probability of occurrence
Approach 3: Correlate the wind condition to a corresponding sea state using fits based on site specific scatter diagrams (mean fit). | Approach 4: Calibration of Approach 3 to ensure that the simplified wave climate produces the expected site specific wave fatigue loading (best fit).
Vh
Hs
Vh
Hs

## Slide 6
Site Specific Data
Wind and Wave Data (LIDAR / Hindcast):
Simplified Data for Fatigue Analysis
Simplified wind/wave climate for analysis
Substructure Design
Fatigue Damage Calculation and consequent Design
Too complex to analyse all combinations
Traditionally considered by defining wind conditions and superimposing wave conditions: Wave probability subservient to wind.
Traditional Analysis Approach

## Slide 7: Mean Fit Analysis Approach
Tz
Hs
50% Probability of Non-Exceedance Fit on the Metocean Scatter Table

## Slide 8
Chart: Tz – Hs: Relationship
| 0.25 | 0.75 | 1.25 | 1.75 | 2.25 | 2.75 | 3.25 | 3.75 | 4.25 | 4.75 | 5.25 | 5.75 | 6.25 | 6.75 | 7.25 | 7.75 | 8.25
Tz(Hs) at 50% of non-exceedance | 2.2856 | 2.9758 | 3.6398 | 4.4446 | 4.9996 | 5.5652 | 6.2341 | 6.5925 | 7.2067 | 7.5403 | 7.9172 | 8.3378 | 8.4739 | 8.9143 | 9.1619 | 9.4571 | 10.1
Mean Fit Analysis Approach
Chart: Hs – Vh: Relationship
| 0.5 | 1.5 | 2.5 | 3.5 | 4.5 | 5.5 | 6.5 | 7.5 | 8.5 | 9.5 | 10.5 | 11.5 | 12.5 | 13.5 | 14.5 | 15.5 | 16.5 | 17.5 | 18.5 | 19.5 | 20.5 | 21.5 | 22.5 | 23.5 | 24.5 | 25.5 | 26.5 | 27.5 | 28.5 | 29.5 | 30.5 | 31.5 | 32.5 | 33.5 | 34.5 | 35.5 | 36.5
50% Non exceedance MEAN Fit | 0.4791 | 0.48284 | 0.50244 | 0.53433 | 0.60232 | 0.681 | 0.76843 | 0.84314 | 0.91751 | 1.0013 | 1.1393 | 1.251 | 1.3714 | 1.4702 | 1.6302 | 1.752 | 1.8593 | 1.9934 | 2.0995 | 2.2251 | 2.3361 | 2.4292 | 2.4916 | 2.7309 | 2.8716 | 2.9128 | 2.9603 | 2.973 | 2.9958 | 3.2589 | 3.4625 | 3.4688 | 3.7222 | 3.6875 | 3.5 | 3.8333 | 3.75

## Slide 9: Wave Fatigue Analysis – Mean Fit
Polynomial relationships used to relate wind speed to sea state definition
The probability of the resulting wave climate is then subservient to the wind probability distribution
Spectral wave fatigue analysis is performed for comparison of simplified wave climate with site specific fatigue lives
Joint locations and notations

## Slide 10: Mean Fit Fatigue Analysis Limitations
** Orange cells: Non-conservative results
Wave Fatigue Analysis – Mean Fit Results

## Slide 11: Mean Fit Fatigue Analysis Limitations
The mean fit approach results in the number of large wave heights being under-predicted compared to the direct Metocean wave data
Calibration is required to correct this under-prediction: find the best fit relationship between wind speed and wave height to give the expected fatigue lives due to wave only
Combined wind wave fatigue would then be expected to give a better estimate of overall fatigue irrespective of whether wind or wave condition dominate

## Slide 12: Atkins Calibration Methodology – Best Fit
Site Specific Wind Data
Establish Wind / Wave Polynomial relationship at
% of Non Exceedance
Wind Dependent Wave Data
Fatigue Analysis
Wave only Fatigue Lives
Site Specific Wave Data
Fatigue Analysis
Expected wave only Fatigue Lives
Compare Fatigue Lives
Iterate: Change % of Non Exceedance until fatigue lives are similar
Non
Comparable
Comparable
Using Metocean Data directly
Using Wave Data related to Wind Speeds

## Slide 13: Calibrate the Wind Wave relationships Best Fit Analysis Approach
% Probability of Non-Exceedance Fit on the Metocean Scatter Table calibrated to obtain the best fit on fatigue lives
Chart: Hs – Vh: Relationship
| 0.5 | 1.5 | 2.5 | 3.5 | 4.5 | 5.5 | 6.5 | 7.5 | 8.5 | 9.5 | 10.5 | 11.5 | 12.5 | 13.5 | 14.5 | 15.5 | 16.5 | 17.5 | 18.5 | 19.5 | 20.5 | 21.5 | 22.5 | 23.5 | 24.5 | 25.5 | 26.5 | 27.5 | 28.5 | 29.5 | 30.5 | 31.5 | 32.5 | 33.5 | 34.5 | 35.5 | 36.5
78% Non exceedance BEST Fit | 0.89524 | 0.90334 | 0.91492 | 0.92933 | 0.9596 | 1.0138 | 1.1563 | 1.2614 | 1.3758 | 1.4781 | 1.6243 | 1.7774 | 1.9263 | 2.1248 | 2.3326 | 2.4287 | 2.6749 | 2.9312 | 3.0921 | 3.2684 | 3.5484 | 3.6823 | 3.7097 | 4.0345 | 4.1147 | 4.0808 | 3.8443 | 3.6825 | 3.543 | 3.9479 | 4.89 | 4.22 | 5.36 | 4.01 | 3.92 | 4.34 | 3.89
50% Non exceedance MEAN Fit | 0.4791 | 0.48284 | 0.50244 | 0.53433 | 0.60232 | 0.681 | 0.76843 | 0.84314 | 0.91751 | 1.0013 | 1.1393 | 1.251 | 1.3714 | 1.4702 | 1.6302 | 1.752 | 1.8593 | 1.9934 | 2.0995 | 2.2251 | 2.3361 | 2.4292 | 2.4916 | 2.7309 | 2.8716 | 2.9128 | 2.9603 | 2.973 | 2.9958 | 3.2589 | 3.4625 | 3.4688 | 3.7222 | 3.6875 | 3.5 | 3.8333 | 3.75
Chart: Tz – Hs: Relationship
| 0.25 | 0.75 | 1.25 | 1.75 | 2.25 | 2.75 | 3.25 | 3.75 | 4.25 | 4.75 | 5.25 | 5.75 | 6.25 | 6.75 | 7.25 | 7.75 | 8.25
40% Non exceedance; BEST Fit | 2.2856 | 2.9758 | 3.6398 | 4.4446 | 4.9996 | 5.5652 | 6.2341 | 6.5925 | 7.2067 | 7.5403 | 7.9172 | 8.3378 | 8.4739 | 8.9143 | 9.1619 | 9.4571 | 10.1
50% Non exceedance; MEAN Fit | 2.4404 | 3.1995 | 3.7999 | 4.5974 | 5.228 | 5.7434 | 6.4206 | 6.7652 | 7.3801 | 7.6998 | 8.1295 | 8.4745 | 8.6216 | 9.1111 | 9.3095 | 9.5714 | 10.25

## Slide 14
** Orange cells: Non-conservative results
* Green Cells: Conservative Results
Wave Fatigue Analysis – Best Fit Results

## Slide 15
A technique has been developed for calibrating the above simplified sea state definition using spectral fatigue analysis methods.
This calibration of wave height, period and direction against site specific scatter tables derives polynomial relationships between the variables based on percentages of non-exceedance.
The spectral fatigue analysis has been carried out using ANSYS ASAS suite and Pierson Moskovich Sea State definition.
Best Fit Fatigue Analysis

## Slide 16: Directionality
ACTUAL Wind | ACTUAL Wave | Modelled Wave
Calibration is also used to compensate for wave directionality simplifications and the effects it may have on fatigue damage
This is done comparing the simulated wave magnitudes and directions with the full directional scatter data from the Metocean information
Site-2
Site-1
Site-1
Site-2

## Slide 17
Establishing a simplified correlation between the wind and wave conditions is a pre-requisite for any type of coupled analysis process.
    Site specific correlation models based on simplified directional combinations as well as simplified sea state to wind speed relationships have been shown to be a viable and advantageous way to achieve the required correlation.
  Calibration is required to create simplified wave height-wind speed models that produces similar wave only fatigue damage compared with the actual.
    Mean fit relationships between Hs and Vh (50%-50%) give significantly non-conservative fatigue lives.
Wave period relationships can be used to control the balance of fatigue lives towards the top of the structure, relative to the bottom.
    This is expected, as these low period / steep waves will have higher surface velocities, but will not be felt as much at depth as longer period waves, which will be more dominant for global effects.
      The calibration exercise can also compensate for the potential differences in a simplified directional model.
    The wave rose resulting from this simplified approach to wave definition may be slightly different from the site specific wave rose but fatigue lives will be similar
Conclusions

## Slide 18: Thank you Any Questions?
If you would like to find out more about Atkins Offshore renewables, please visit:
www.atkinsglobal.co.uk/en-GB/group/sectors-and-services/sectors/energy/renewables