## Slide 1: Machine Learning Algorithms for Wind Turbine Performance Enhancement Optimization of wind turbine performance based on SCADA data
Sebastian Kaus, Specialist Wind Farm Performance Monitoring
WindEurope Summit Hamburg
September 29th 2016

## Slide 2: Target of presentation
How Senvion uses machine learning algorithms for turbine performance monitoring
How Senvion machine learning techniques improve the yield of a wind turbine

## Slide 3: Agenda
Introduction
Machine learning approach for performance monitoring
Case study – Detection of yaw misaligment
Summary

## Slide 4: Agenda
Introduction
Machine learning approach for performance monitoring
Case study – Detection of yaw misaligment
Summary

## Slide 5: OEM has ideal preconditions for Big Data & Machine Learning
Turbine Master Data
SCADA Data
Large Fleet
Turbine Parameter Set
Technical Knowledge
Feedback from Service
Notes: Turbine parameter set : Defines how the turbine behaves
Turbine Master data: Defines where turbine is located and what kind of turbine we‘re analyzing
We‘re not only having a lot of data per turbine, we have a lot of data because we have a large fleet
We know what that data acutally means, because we have the technical knowledge about the turbines
Ultimaltely, we also have access to service data, we can compare and analyse maintenance events with data

## Slide 6: Agenda
Introduction
Machine learning approach for performance monitoring
Case study – Detection of yaw misaligment
Summary

## Slide 7: Self learning algorithm improves over time
Wind farm
data
Calculation of Key Performance Indicators
Data Base
Evaluation with
machine learning
algorithm
AdvancedMonitoringService
Corrective action
Sensor & Plausibility
Analysis
  KPI for specific turbine anomalies e.g. yaw or pitch misalignment

## Slide 8: Key Performance Indicators „sharpen the picture“
Vane position
KPI‘s
  Reduction of noise in data set
  KPI work like a low pass filter
~-20%
Reference
  Less computing time to train model
  Less data points, but more meaningful data
Error rate in classification
Power
Wind Speed
Multiple days
9331
Time (s)
SCADA
KPI
SCADA
KPI
1,68

## Slide 9: Agenda
Introduction
Machine learning approach for performance monitoring
Case study – Detection of yaw misaligment
Summary

## Slide 10: Case Study – 5° Yaw misalignment successfully detected
Support Vector Machine
Neural Network
Naïve Bayes
Decision Tree
Random Forrest
Training Set
8 wind farms with aligned and misaligned turbines
1100 KPI used to train model
Case conditions
Wind farm with 12 turbines
Turbine #8 purposly misaligned by 5°
2 Week misalignment
Input data misaligned turbine
10 Minute Standard SCADA Data
Converted into 11 KPI
Analysis
Ensemble of selected machine learning algorithms
Analysis result
+1% AEP
(-Criteria)
Notes: Wie viel bringt 5° im Feld?  1% AEP

## Slide 11: Agenda
Introduction
Machine learning approach for performance monitoring
Case study – Detection of yaw misaligment
Summary

## Slide 12: Summary & Conclusion
Summary
OEM has ideal preconditions for Big Data & Machine Learning
Machine learning techniques enable automated complex analysis without installing additional hardware or software
Conclusion
Use of machine learning algorithms on combination of all available turbine data across the fleet
Senvion Advanced Monitoring Service increases the yield of turbines with specific fault analysis and fast resolving due to integrated service
Thank you very much!