## Slide 1: A Modified Levelized Cost of Energy (LCOE) Model to Provide Bid Comparisons for Power Purchase Agreements
Maira Bruck, Navid Goudarzi, Peter Sandborn
Center for Advanced Life Cycle Engineering (CALCE), Mechanical Engineering Department, University of Maryland

## Slide 2: Levelized Cost of Energy (LCOE) and Power Purchase Agreements
Levelized Cost of Energy (LCOE):
“The Total Life-Cycle Cost (TLCC) for each unit of energy produced in the given lifetime of a project.”
Power Purchase Agreements (PPAs):
PPAs are performance-based contracts that aim to create a “fair” agreement for the purchase and sale of energy between a utility (the Buyer) and a generator (the Seller)
  LCOE is commonly used within these energy contracts to determine a fair Cost of Energy (COE)
PPAs define under (minimum) and/or over (maximum) energy delivery limits and their penalties
  Over production causes a loss as the energy will no longer be bought (or will be bought at a reduced rate)
  Under production will cause the Seller to be charged a penalty

## Slide 3: The Problem with LCOE
Energy delivery limits in PPAs increase the LCOE through production loss and penalties, which should be considered costs
  Conventional LCOE calculations do not include the penalties
  An accurate LCOE is vital to ensure that the project breaks even and does not fail
  An LCOE that is too high might deter potential investors or Buyers in the PPA
  An LCOE that is too low hurts the Seller
In a bidding market for PPAs on a wind farm, either the wind farm or the utility bids a contract that presents an escalating (with “inflation”) price schedule or a constant price schedule
  Utilities prefer an escalating price schedule because investors and utilities look at short-term returns instead of long-term returns
  The wind farm needs an accurate LCOE to compare proposed price schedules in order to ensure that there is a similar total revenue from the escalating versus a flat price schedule
Creating a price schedule in which the final net revenue equals the net revenue from a constant LCOE (throughout the contract length) is generally not possible
Revenue has to be based on purchased energy, conventional LCOE is based on produced energy.
Notes: Inflation is both the change in the purchasing power of money AND inflation in O&M costs incurred.
Buyers can get a better short-term return if the price schedule escalates (front load)
Sellers want to make sure that the total after 20 years is the same as the flat price schedule (LCOE based)
It is incorrect to calculate revenue based on produced energy, it has to be calculated based on energy that is sold. LCOE is calculated for all produced energy.

## Slide 4: Modeling LCOE
CPE = Cost to produce energy
E = Energy generated
r = WACC
I = Initial investment cost
OM = Operation and maintenance cost
F = Fuel cost
TC = Tax credit
The LCOE is the cost that, if assigned to every unit of energy produced by the system over the analysis period, will equal the total life-cycle cost when discounted back to the base year.
Chart: Year of Project Under PPA
75% of expected output | 937950 | 937950 | 937950 | 937950 | 937950 | 937950 | 937950 | 937950 | 937950 | 937950 | 937950 | 937950 | 937950 | 937950 | 937950 | 937950 | 937950 | 937950 | 937950 | 937950
52% of expected output | 650312 | 650312 | 650312 | 650312 | 650312 | 650312 | 650312 | 650312 | 650312 | 650312 | 650312 | 650312 | 650312 | 650312 | 650312 | 650312 | 650312 | 650312 | 650312 | 650312
Annual kWh Output | 1367060 | 765980 | 897600 | 635070 | 924500 | 1276000 | 712300 | 912400 | 846580 | 512300 | 765890 | 987650 | 812340 | 743500 | 654000 | 600320 | 590870 | 637000 | 660120 | 680130
Conventional Model:
New Model:
PPA Penalties:
Maxlim = Maximum Energy Threshold
Minlim = Minimum Energy Threshold
PN = Penalty cost
PL = Production loss
Pexp = Expected energy production
COE = Cost of energy
Maximum Energy Threshold
Minimum Energy Threshold
Annual Output
Notes: n is the years
PL is the Production Loss, so it is the Maximum limit (it is a direct and opportunity cost)
PN is the Penalty is it is the Minimum limit.
PN and PL terms are added to CPE because they are extra costs
Could use a fraction of COE in the PL calculation to model the ability to sell at a lower price
Could use a multiplier on COE if under delivery requires purchase of power at a higher price (current equation implicitly assumes you are penalized at the COE)
COE is in the contract (CPE is an actual realized by the seller)

## Slide 5: New LCOE Model Results
The new LCOE model depends the capacity factor variation and the penalty “gap” (the difference between the minimum and maximum penalty thresholds). For a symmetric gap:
Penalty gap size = Maxlim – Minlim
Capacity Factor = 0.2
Half the time, the energy production is above or below the average production determined by the capacity factor by the variation specified
I = $1500 per installed kW
OM = $0.01 per kWh produced
F = $0
TC = $0.05 per kWh sold
r = 0.089 per year
RP = rated power
Penalty Gap Size:
Annual Energy Output Variation:
Notes: Graph 1
Orange line slope down due to discount rate (same thing on the right most point of the right graph)
In each year you assumed

## Slide 6: Wind Farm Case Study
Maxlim = 0.75
Minlim = 0.52
I = $1500 per installed kW
OM = $0.01 per kWh produced
F = $0
TC = $0.05 per kWh sold
r = 0.089 per year
Farms differ and different contracts need to be constructed for them
The conditions in the farms determine the gap between the conventional LCOE and an LCOE that includes delivery penalties
In the PPA bidding market, the conventional LCOE could be problem (wind farms 1,2,3, and 6)
Actual wind farm data shows that the LCOE without penalties (conventionally calculated LCOE) is lower than the actual LCOE that includes penalties. Different wind farms have different characteristics and the gaps in the actual LCOE can vary.
Notes: Left circled case – the production keeps falling below the min penalty, but never exceeds the max
Right circled case, the production is between the min and max all the time, so the do nothing. If you reduced the gap, the points would separate.
The green triangles are the basis for the PPA today. In the bidding market, you would not want to use this LCOE (except for the right circled case, 4 and 5 are good too).

## Slide 7: Conclusions
By creating mechanisms to reduce the risk of higher costs for the Buyer, PPAs create a paradox of higher LCOEs for the Seller
The new LCOE model allows Sellers in a PPA to use expected future energy production to assist in negotiating penalties and an appropriate Cost of Energy in the PPA based on the expected costs from penalties
The optimal PPA should focus on an appropriate Minlim for projects with a low capacity factor and projects with a higher capacity factor can address having both limits or just one limit depending on the expected variation and the Buyer’s need for energy
Energy Markets Impact: The new LCOE model also allows for the Seller to compare contract bids with differing price schedules. This allows the Sellers to choose a price schedule that results in a final net revenue that is close to the net revenue from a flat price schedule.
Notes: Flat price schedule = constant LCOE over the whole contract