## Slide 1: Relevance of LCOEs for Energy Markets – today and in the future
Prof. Graham Weale
Ruhr University Bochum, Germany Wind Europe Summit 2016, Hamburg 29th Sept.

## Slide 2: Agenda
Who uses LCOEs and how?
Short-term relevance
Long-term relevance – looking beyond electricity markets
Will LCOEs continue to be the key metric for the future?

## Slide 3: 1. Who uses LCOE and how?
Governments, as as key metric for the cost of energy transitions
  Relevant so long as focus is on cost / MWh
  Used to make choice between different types of plants
  Principal metric for auctions
Project developers and utilities/customers signing PPAs on fixed cost basis
  Limited PPAs in Europe, not all fixed cost
  US Wind PPAs at $ 20-25/MWh (helped by production tax credits)
  US Solar PPA at $ 37/MWh (helped by investment tax credits)

## Slide 4: Example from Germany (2014): LCOEs used to plan future average RES costs - aim of €12cts/kWh
EEG Renumeration system for new plants from 2015
Average depends upon mix of RES technology
Production in TWh
Remuneration in €cts/kWh

## Slide 5: LCOE's and their limitations
LCOE – well-established parameter for full ex ante cost of electricity
Calculates cost rather than value of power produced
  Cost and value will differ – more for non-dispatchable plants
  Storage and balancing costs may need adding
  Other than through carbon price does not reflect environmental costs
LCOE depends on input assumptions (not all known exactly in advance)
  Out-turn will always be different from plan!
  But in auction (or PPA) determines what operator is paid / MWh
  Cost of capital (r) is crucial

## Slide 6: Impact of wind energy on the spot price (DE, 2015) - increases disconnect between value and LCOE
Source: Übertragungsnetzbetreiber, EPEX Spot, BDEW (eigene Berechnungen)
Chart: 
22 €/MWh
42 €/MWh
36.955 MW (max. production)
177 MW (min. prod.)
Wind Production in MW
€ / MWh
© Prof. Graham Weale
Wind Europe Summit 2016 - LCOEs in the Context of EU Energy Markets
6

## Slide 7: 2. Short-term relevance of LCOE's - poor connection to wholesale / consumer prices
Wholesale price – set by SRMC weighed down by plants with zero SRMC
  Unique feature of electricity markets: SRMC << LRMC
    Unless adequate infra-marginal rents and scarcity pricing achieved
Consumer variable price (excluding network and retail costs)
  Combination of wholesale prices, renewables subsidies and other taxes
LCOE has very little short-term impact on wholesale / consumer prices
  Consumers do not see the LCOE and cannot respond in classic manner
    Unless they contract with a PPA and by-pass the other markets

## Slide 8: Indicative LCOE's, wholesale price and consumer prices for energy element excluding pure taxes
LCOE Wholesale Consumer
Chart: €/MWh
| CCGT | Nuclear | Onshore wind | Offshore wind | PV (Ground-mtd) | Wholesale price | Small | V. large
€/MWh | 62 | 50 | 50 | 85 | 75 | 25 | 140 | 50
 | 60 | 30 | 35 | 10 | 5
Offshore wind costs include connections to shore

## Slide 9: Slow impact of reducing LCOEs in current system – high legacy of renewables costs
Reductions in LCOEs (of individual technologies and RES overall) only feed into the price system very slowly
  Tipped into „tank“ of all renewables costs which have to be amortised over next 20 years. Example - Germany
Chart: Annual Costs for Renewables in Germany € bn.
| 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020
Biomass | 4.4762 | 5.842 | 6.1584 | 6.378 | 6.1947 | 6.6734 | 6.649 | 6.703 | 6.739 | 6.791
Hydro | 0.23107 | 0.3475 | 0.42023 | 0.401 | 0.43568 | 0.47113 | 0.48 | 0.497 | 0.511 | 0.527
Biogas | 0.03588 | 0.0464 | 0.048167 | 0.0826 | 0.085636 | 0.085729 | 0.083 | 0.083 | 0.082 | 0.082
Geothermie GWh
Wind onshore | 4.1647 | 3.625 | 3.5232 | 4.046 | 4.6391 | 5.3371 | 5.716 | 6.247 | 6.749 | 7.185
Wind offshore | 0.08522 | 0.0952 | 0.1226 | 0.213 | 1.7169 | 2.4132 | 2.958 | 3.497 | 3.939 | 4.254
Solar | 7.7661 | 9.156 | 9.457 | 10.2302 | 10.6048 | 10.5203 | 10.506 | 10.585 | 10.648 | 10.733

## Slide 10: 3. Longer-term relevance of LCOEs
Over time determines what consumers / the economy has to pay for power
  also the political pace of decarbonisation
Contributes to the international competitiveness of a country
Lower LCOEs keep electricity more competitive against other forms of energy
  E.g. natural gas, hydrogen and even energy efficiency investment
    But energy taxation must not stand in way
Helps pave way for a strong electrification policy
  Increase market share of power in final consumption
  Allows more energy to be used without increasing CO2 emissions

## Slide 11: LCOEs for different forms of energy – must look beyond electricity!
Race to the floor – limited global carbon budget limits lead to prospect of lower long-term fossil-fuel prices continuing to challenge renewables
  Offshore wind has to join in the race!
Chart: Energy Costs (before adjusting for efficiency in use)
| Gas | Gas + € 100 CO2 | Nuclear | Onshore wind | Offshore wind | PV (Ground-mtd)
€/MWh | 20 | 40 | 50 | 50 | 85 | 75
 | 60 | 30 | 35 | 10

## Slide 12: 4. Will LCOEs continue to be the key metric?
Yes, so long as focus is on the MWh of energy itself
  But need to make different sources strictly comparable and include appropriate transport, balancing and environmental costs
  Delivered MWh is a solid metric, though value may be very different
Alternative: annual capacity-related payment for availability
    With owners earning directly from wholesale market for MWh produced (and taking market risk)
    Similar to concept for thermal plant capacity payments
    Would focus attention on maximising value of projects
Conclusion: for at least the medium-term LCOEs (with adjustments) are likely to be key metric for plant choice

## Slide 13
THANK YOU FOR YOUR ATTENTION
Graham.Weale@RUB.com