## Slide 1: Experience with methods of assessing complaints of wind farm noise
Friedrich Wilts, Thomas Neumann, Johannes Pohl, Gundula Hübner

## Slide 2: Introduction
Regarding wind turbine noise there are sometimes discrepancies between permitted sound levels and subjective perception of noise.
Two German wind farms were assessed – both in accordance with legal requirements – to identify the factors that lead to complaints.
This presentation is about the methods used in these studies
Notes:   It’s no secret that UL is a global force for good that has been working to promote safe living and working environments for more than a century
    We’ve been a leading standards development organization since the dawn of electricity
    And we’ve been advancing safety breakthroughs and addressing the risks associated with every wave of innovation including electronics, petrochemicals and sustainability
    We work collaboratively with our customers to design, produce, package and sell safer products around the world
    And we consistently fulfill our safety mission by acting in ways that reinforce our ethical values, respect people, empower communities and support the natural environment

## Slide 3: Overview of Methods
Psychological surveys
To collect information on stress effects
Sound recorders and complaint forms
To assess times and sound patterns of individual occurrances of percieved noise disturbance.
Sound measurements
For correlation with WT parameter and periods of percieved noise disturbance.

## Slide 4: Psychological surveys
Residents in the vicinity of the wind farms were interviewed elaborately by psychologists to get information about somatic / psychological stress effects and the most annoying noise characteristics.
The following indicators were used:
    general impact of the wind farm,
    general impact of WT noise,
    WT noise annoyance and its temporal change,
    characteristics of a typical situation with WT noise annoyance,
    psychological and somatic symptoms induced by WT noise,
    cognitive and behavioral coping responses.

## Slide 5: Psychological outcomes
In both studies we found approximately 20 residents who were strongly annoyed by WT noise.
Strongly annoyed means that they reported not only at least medium annoyance but also symptoms induced by WT noise at least once a week.
Most frequently disturbed were sleeping, relaxation, and leisure activities.
Typical symptoms were:
      disturbed sleep,
      fatigue,
      irritability / anger,
      negative mood,
      reduced concentration.

## Slide 6: Standard method of assessing the legality of wind turbines
This approach is adequate in most cases, but sometimes resdients complain about WT-noise, even when regulations are met.
Sound measurements
Measuring the emission of each single WT according to IEC61400-11
Sound prognosis
Calculating the estimated sound immissions caused by wind turbines at residents houses according to ISO9613-3
Regulations
Comparing prognosis results against local regualtions (e.g. TA-Lärm for Germany)

## Slide 7: Aspects not captured with the standard method
The whole sound field can consist of multiple different sound sources.
    In noisy areas an additional sound source (WT) may lead to annoyance
In silent areas WT-noise can have a different effect on residents than in noisy neighborhoods.
People may hear and feel annoyed by a even very quiet wind turbine after being woken due to a rare sound occurrence not linked to wind turbines such as a passing train or plane.
Infrequently occurring sound characteristics such as amplitude modulation (AM) are not an element of standard sound measurements and regulations.

## Slide 8: Permanent sound measurements
To get an overview of the whole soundscape a permanent sound measuring station and evaluation algorithms was developed and installed:

## Slide 9: Experiences with permanent sound measurements
Through the use of the permanent sound measuring device we found:
    data gained was useful to get a better understanding of the emitted sound of the wind farm and the general soundscape
    this method helps to find correlations between different data sets
    at wind speeds above 10 m/s or in rainy conditions the recorded data was strongly disturbed by environmental noise.
In future versions:
    a rain sensor should be attached to the measuring station to filter out time periods disturbed by rain.
    a web interface showing actual and historical data should be developed to allow a better interaction with residents.
It is also desirable to get a better wind shield and to operate simultaneously several measuring stations within one campaign to get a better understanding of directional sound emissions and local effects

## Slide 10: Reasons to asses annoying time periods
To understand disturbing noise phenomena of wind turbines it is essential to know:
    which specific situations are most annoying, such as:
      date/time
      operational state of WT
      environmental conditions
    in which stress state residents are during this time periods. E.g.:
      emotions
      cognitions

## Slide 11: Methods to asses annoying time periods
Complaint sheets
Audio Recorder
2-sided sheets asking for:
WT noise annoyance
noise pattern
disturbed activities
emotions and cognitions
weather conditions
Linear sound recorder equipped with wind shield and stand
Used by residents to record annoying sound patterns with electronic time stamp
Not used to obtain sound levels, but for evaluating sound characteristics

## Slide 12: Experiences with assessing annoying time periods
In our studies we found that very few persons were willing to support the assessments:
    this leads to a very weak (but important) data basis for further analyses.
Residents need to be more motivated to help by reporting annoying time periods. Improvements can be made through:
    Intensifying public information procedures.
    Developing easier methods of reporting such as smart phone applications that incorporate both sound recording and complaint forms.

## Slide 13: Amplitude Modulation
Amplitude modulation is:
different from the “natural” background noise,
very silent
described as swishing
in the frequency of the rotor blades
a temporal change of loudness
Through the reported annoying time periods and sound recordings made by the residents we found, that in many cases amplitude modulation was at least perceptible

## Slide 14: Increasing sound levels Case II
Correlation of the permanent measurements and the reporting of individual occurrances of annoyance showed at least two time periods where the residents were annoyed by increases in sound levels related to the WT:
Increasing wind speed
Reported complaints
slow increase of sound levels

## Slide 15: Conclusions
Different methods were used to objectify noise complaints in two German wind farms, which were both in accordance with the legal requirements.
Psychological surveys collected information about stress effects and annoying situational conditions.
To asses periods of annoyance requires the support of the residents. We tried to motivate residents to fill out complaint sheets and to use sound recorders to report their complaints. However in both studies only very few residents cooperated.
The combination of one or more permanent measurement stations, access to WT performance data and resident reporting is a promising methodology for better understanding the factors that lead to complaints.
There are ideas for improvements like Smartphone-Applications or providing live sound level data to the residents.
Further studies on other wind farms should be conducted to get a better understanding of annoying sound patterns.
The effect of some sound characteristics such as amplitude modulation requires further research.

## Slide 16: Thank you.