## Slide 1: Near flow measurements with nacelle lidars: the future of power performance verification?
A. Borraccino, R. Wagner, DTU Wind Energy, borr@dtu.dk D. Schlipf, F. Haizmann, Stuttgart Wind Energy
5-beam Avent demonstrator
ZephIR Dual-Mode

## Slide 2: Searching for free stream wind speed
Add Presentation Title in Footer via ”Insert”; ”Header & Footer”
??
Modern turbines: 2.5D ~ 200-400m
Decorrelation WSpeed / power
Hhub speed insufficient?
2.5D not really free wind …

## Slide 3: Does this make it any easier?
Add Presentation Title in Footer via ”Insert”; ”Header & Footer”
Perdigão. credit: N. Vasiljevic
In complex terrain:
  any ”free stream” wind speed idea?
  site calibration? Maybe
Offshore:
  mast expensive
  free wind may not be measurable due to wakes

## Slide 4: Power performance verification: nacelle-mounted lidars, the future?
Add Presentation Title in Footer via ”Insert”; ”Header & Footer”
Several possibilities for lidar measurements:
2.5D distance fitting wind speed + direction + shear to lidar-measured LOS velocities
lidar measurements

## Slide 5: Power performance verification: nacelle-mounted lidars, the future?
Add Presentation Title in Footer via ”Insert”; ”Header & Footer”
Several possibilities for lidar measurements:
2.5D distance fitting wind speed + direction + shear to lidar-measured LOS velocities
Multiple distances close to rotor induction integrated in wind field reconstruction
lidar measurements
induction transfer function to retrieve

## Slide 6: Case 1: lidar meas. @2.5D
Add Presentation Title in Footer via ”Insert”; ”Header & Footer”
  5B-Demo: use the 5 pts ZDM: use 10 pts
lidar measurements

## Slide 7: Case 1: lidar meas. @2.5D Mast comparison
Add Presentation Title in Footer via ”Insert”; ”Header & Footer”
  5B-Demo: use the 5 pts ZDM: use 10 pts HWS estimated @hub height

## Slide 8: Case 1: lidar meas. @2.5D Power curves
Add Presentation Title in Footer via ”Insert”; ”Header & Footer”

## Slide 9: Case 2: lidar meas. @ multiple distances close to rotor
Add Presentation Title in Footer via ”Insert”; ”Header & Footer”
  5B-Demo : use the 5 pts ZDM: use 10 pts @[0.5 0.75 1.0 1.15] D @[0.3 1.0 1.25] D
lidar measurements
induction transfer function to retrieve

## Slide 10: Case 2: lidar meas. @ multi-dist (near flow) Mast comparison
Add Presentation Title in Footer via ”Insert”; ”Header & Footer”
  5B-Demo: use the 5 pts ZDM: use 10 pts @[0.5 0.75 1.0 1.15] D @[0.3 1.0 1.25] D HWS estimated @hub height and @2.5D distance

## Slide 11: Case 2: lidar meas. @ multi-dist (near flow) Power curves
Add Presentation Title in Footer via ”Insert”; ”Header & Footer”

## Slide 12: AEP results
Add Presentation Title in Footer via ”Insert”; ”Header & Footer”
IEC -12-1 methodology
extrapolated AEPs
0.5 m/s bin width
Relative difference in % of cup-based AEP
AEP estimations as good with the “multi-distances” method as with the 2.5D (<1.5% difference)
Lidar measurements | @2.5 D (case 1) |  |  | @multiple distances (case 2) |  | 
Rayleigh avg wind speed | 6 m/s | 8 m/s | 10 m/s | 6 m/s | 8 m/s | 10 m/s
Avent 5-Beam demonstrator lidar | Wspeed difference: +1.2% |  |  | Wspeed difference: +0.1% |  | 
 | -2.0% | -1.6% | -1.2% | -0.4% | -0.1% | +0.0%
Zephir Dual Mode lidar | Wspeed difference: +0.1% |  |  | Wspeed difference: -0.7% |  | 
 | +0.4% | +0.2% | +0.1% | +2.0% | +1.3% | +0.9%

## Slide 13: Take-aways
Add Presentation Title in Footer via ”Insert”; ”Header & Footer”
is found! The solution: measurements close to rotor, within the induction zone, at multiple distances, e.g. with nacelle lidars
Wind Field Reconstruction algo. provide estimates comparable classic mast instrumentation ( difference)
Power curves in flat terrain verified accurately, reduced scatter (as usual with nacelle lidars)
next generation of IEC61400-12-1 standards? (NWIP)
Further work :
  Two-dimensional induction? (ongoing)
  Adaptation and testing of method in complex terrain (campaign in Hill of Towie, Zephir DM+4-beam Wind Iris)
  Uncertainty assessment of Wind Field Characteristics: speed, direction, shear, induction factor / Ct, …

## Slide 14: Thanks for your attention!
Add Presentation Title in Footer via ”Insert”; ”Header & Footer”
  More info:
  website www.unitte.dk
  contact borr@dtu.dk
5B-Demo
ZDM
Mast

## Slide 15: Acknowledgements
Add Presentation Title in Footer via ”Insert”; ”Header & Footer”
This work was performed within the UniTTe project (www.unitte.dk) which is financed by Innovation Fund Denmark.

## Slide 16: Model-based wind field reconstruction
Add Presentation Title in Footer via ”Insert”; ”Header & Footer”
Doppler wind LiDaRs do not…
…measure wind speed, wind direction, shear, …
see Hardesty, 1987 (wonderful description of lidar principles)
They:
  only measure LOS velocities
  estimate/reconstruct wind field characteristics (WFC)

## Slide 17: Model-based wind field reconstruction
Add Presentation Title in Footer via ”Insert”; ”Header & Footer”
Modelling the wind field
  choose a wind model that fits the application & site characteristics
  the reconstruction should be performed either in the WIND coordinate systems or in the HUB
For power performance: static models
  i.e. no time dependency
  use 10-min averages of:
    LOS velocities
    inclinometers readings
  use knowledge of the trajectory (opening angles, ranges config) and of lidar position

## Slide 18: Model-based wind field reconstruction
Add Presentation Title in Footer via ”Insert”; ”Header & Footer”
Wind models
fitted wind characteristics are:
    HWS
    yaw misalignment (relative wind dir)
    shear exponent
Model |  |  |  | comment
Homogeneous 2D |  |  |  | Does not depend on X, Y, Z
Homogeneous 3D |  |  |  | Does not depend on X, Y, Z
Inhomogeneous 2D + linear V shear |  |  |  | Yaw misalignment
Inhomogeneous 2D + linear V shear + linear V veer |  |  |  | Yaw misalignment
Inhomogeneous 2D + power law shear |  |  |  | Yaw misalignment
Model |  |  |  | comment
Homogeneous 2D |  |  |  | Does not depend on X, Y, Z
Homogeneous 3D |  |  |  | Does not depend on X, Y, Z
Inhomogeneous 2D + linear V shear |  |  |  | 
Inhomogeneous 2D + linear V shear + linear V veer |  |  |  | 
Inhomogeneous 2D + power law shear |  |  |  | 

## Slide 19: Model-based wind field reconstruction
Add Presentation Title in Footer via ”Insert”; ”Header & Footer”
Wind models
fitted wind characteristics are: free stream HWS , yaw misalignment , shear exponent , induction factor .
Model name |  |  |  | comment
Homogeneous 2D |  |  |  | Does not depend on X, Y, Z
Homogeneous 3D |  |  |  | Does not depend on X, Y, Z
Inhomogeneous 2D + linear V shear |  |  |  | Yaw misalignment
Inhomogeneous 2D + linear V shear + linear V veer |  |  |  | Yaw misalignment
Inhomogeneous 2D + power law shear |  |  |  | Yaw misalignment
Inhomogeneous 2D + power law shear + induction model |  |  |  | 1D Biot-Savard for induction fct
Model name |  |  |  | comment
Homogeneous 2D |  |  |  | Does not depend on X, Y, Z
Homogeneous 3D |  |  |  | Does not depend on X, Y, Z
Inhomogeneous 2D + linear V shear |  |  |  | 
Inhomogeneous 2D + linear V shear + linear V veer |  |  |  | 
Inhomogeneous 2D + power law shear |  |  |  | 
Inhomogeneous 2D + power law shear + induction model |  |  |  | 1D Biot-Savard for induction fct

## Slide 20: Power performance verification: “standard” procedure, what’s the problem?
Add Presentation Title in Footer via ”Insert”; ”Header & Footer”
Decorrelation WSpeed / power
Hhub speed insufficient?
2.5D not really free wind …
Too expensive: e.g. offshore
??
Modern turbines: 200-400m

## Slide 21: Power performance verification: “standard” procedure, what’s the problem?
Add Presentation Title in Footer via ”Insert”; ”Header & Footer”
??
?
Modern turbines: 2.5D ~ 200-400m

## Slide 22: Nørrekær Enge campaign (NKE), 7 months
Add Presentation Title in Footer via ”Insert”; ”Header & Footer”
Two nacelle lidars: Avent 5-beam (5B) in blue, ZephIR Dual Mode (ZDM) in red
IEC compliant mast + SCADA + full loads

## Slide 23: Power performance verification: nacelle-mounted lidars, the future?
Add Presentation Title in Footer via ”Insert”; ”Header & Footer”
Several possibilities for lidar measurements:
2.5D distance incl. shear
1D distance (only) + correct with induction transfer function
Multiple distances from 0.5 to 1.5D induction integrated in wind field reconstruction

## Slide 24: A simple induction model
Add Presentation Title in Footer via ”Insert”; ”Header & Footer”
Derived from the Biot-Savart law
  see The upstream flow of a wind turbine: blockage effect
  two parameters: induction factor , free wind speed
  , with
What does the induction looks like in NKE?
Black: theoretical,
Colored lines: different 10min periods
Fitting and should be possible