## Slide 1: Offshore wind innovation for cost reduction
What are the knobs to turn? Offshore wind innovation to 2030
Kate Freeman, Junior Associate – BVG Associates
Emilien Simonot, Technology Officer – KIC InnoEnergy
Session title: Optimising O&M to reduce LCOE
29/09/2016, WindEurope 2016

## Slide 2: Who we are
About KIC InnoEnergy
Europe’s engine for innovation in sustainable energy
Empowering every stage of the innovation process
Investing in people, technologies, businesses
Established 2010: supported by the EIT
Public-private partnership aiming for financial sustainability
Notes: Our goal is simple - to achieve a sustainable energy future for Europe
We do that by encouraging innovation – it is the driving force of KIC InnoEnergy
Everything we do is about creating the right conditions for new ideas to flourish
We have a complete package of solutions and services to support innovation at every stage of the journey – from classroom to customers
We help develop new ideas, products and solutions that make a real difference as well as new businesses and new people to deliver them to market
We were established in 2010 and we are supported by the European Institute of Innovation and Technology (EIT)
We are partly funded by the EIT, by our 27 shareholders across Europe and increasingly by the returns on investment we make in new products and solutions and in new businesses

## Slide 3: Who we are
About BVG Associates
Business advisory
Analysis and forecasting
Strategic advice
Business and supply chain development
Economics
  Socioeconomics and local benefits
  Technology and project economic modelling
  Policy and local content assessment
Technology
  Engineering services
  Due diligence
  Strategy and R&D support
Notes: Our goal is simple - to achieve a sustainable energy future for Europe
We do that by encouraging innovation – it is the driving force of KIC InnoEnergy
Everything we do is about creating the right conditions for new ideas to flourish
We have a complete package of solutions and services to support innovation at every stage of the journey – from classroom to customers
We help develop new ideas, products and solutions that make a real difference as well as new businesses and new people to deliver them to market
We were established in 2010 and we are supported by the European Institute of Innovation and Technology (EIT)
We are partly funded by the EIT, by our 27 shareholders across Europe and increasingly by the returns on investment we make in new products and solutions and in new businesses

## Slide 4: Offshore wind innovation to 2030
Need for dramatic cost reduction in offshore wind to compete in the energy market.
The industry has been achieving this through technological innovation (as shown by increases in turbine rating) and by supply chain effects.
1. Problem
What’s next?

## Slide 5: Offshore wind innovation to 2030
1.1 Methodology - overview
A unique approach: Innovations’ impact described through technology AND business perspective.
www.kic-innoenergy.com/reports
Baseline Offshore Wind Farms
As a combination of:
WTG size
4, 6, 8, 10 MW
Sites
40km fr/shore – 25m depth
120km fr/shore – 35m depth
FID dates
2014/20/25/30
Future Offshore Wind Farms
Innovations’ impact
WACC
Supply chain
Permitting
Decom.

## Slide 6: Offshore wind innovation to 2030
1.2 Methodology - example
Innovation: Improvements in range of working conditions for support structure installation vessels
(For a WF on Site Type A, with Turbine Size of 10MW and FID in 2025 compared to same WF in 2014)
Effect on construction CAPEX:
Maximum technical potential impact  9.6%
x Relevance to Site Type A and 10MW-Size Turbine is 83%  7.9%
x Commercial readiness at FID in 2025 is 92%  7.3%
x Market share for project using 10MW-Size WTG - FID 2025 is 78%  5.7%
Anticipated impact on construction CAPEX  5.7%
New CAPEX
New LCOE
(Same for all innovations’ impact on CAPEX, OPEX, AEP)

## Slide 7: Offshore wind innovation to 2030
1.3 Methodology – do it yourself
Cost reduction analysis toolbox
Future renewable energy costs series
How technology innovation is anticipated to reduce the cost of energy in Europe
www.kic-innoenergy.com/reports
Developed in collaboration with
Online LCOE model for evaluation of impact of innovation
www.kic-innoenergy.com/delphos
Objective: understand the impact of what we do
Prioritize
Invest
Take decisions
Serve as reference
Provide:
Reference cost breakdown of renewable energy power plants (EU representative)
List of innovations + impact description
Fully customisable

## Slide 8: Offshore wind innovation to 2030
2.1 Top contributing innovations
Anticipated impact of technology innovations for a wind farm using 10MW-Size Turbines with FID in 2030, compared with a wind farm with 4MW-Size Turbines with FID in 2014, both on Site Type D

## Slide 9: Offshore wind innovation to 2030
Improvement in drive trains | Improvement in components
Many different types of possible drive trains: DC, mid-speed, continuous, superconducting Only some will be taken up by the market, but overall improvements in drive train will be large | Non-offshore-wind specific innovation (metallurgy, tribology) Offshore-wind specific innovation in component design
2.2 Impact of innovation in nacelle
11 innovations
-6% from present to 2030
Highlights:

## Slide 10: Offshore wind innovation to 2030
Blade aerodynamics | Blade manufacture
Blades enabling additional energy production with some cost increase | Blades with lower cost or higher quality through novel materials and processes
2.3 Impact of innovation in rotor
9 innovations
-7.4% from present to 2030
Highlights:

## Slide 11: Offshore wind innovation to 2030
2.4 Impact of innovation in plant development
Array layout | Greater focus on optimisation during FEED
Decreased LCOE through multi-variable optimisation of array layout | Improved decision making through more detailed design
6 innovations
-3.1% from present to 2030
Highlights:

## Slide 12: Offshore wind innovation to 2030
2.5 Impact of innovation in BoP
Improvement in support structure design | Improvement in jacket manufacturing
For all foundation types, design can reduce cost. | For jacket support structures in particular, innovation in manufacturing for modular and pre-fabricated construction is vital.
8 innovations
-3.8% from present to 2030
Highlights:

## Slide 13: Offshore wind innovation to 2030
2.6 Impact of innovation in construction
Working conditions for vessels | Jacket installation
Enabling vessels to work in more extreme weather conditions | Vessel cost and carrying capacity optimised for jacket installation
8 innovations
-2.3% from present to 2030
Highlights:

## Slide 14: Offshore wind innovation to 2030
2.7 Impact of innovation in OMS
Personnel access | Condition based maintenance
Improved personnel access through far from shore techniques, walkways, lifting pods and transfer vessels | Focus maintenance where it is of most benefit
9 innovations
-4% from present to 2030
Highlights:

## Slide 15: Offshore wind innovation to 2030
3.1 Summary & conclusions
1
Inherited
Cost reduction coming from innovation developped on previous WTG series
Comparison to WF with 4 MW WTG – site type A – FID 2014

## Slide 16: Offshore wind innovation to 2030
3.1 Summary & conclusions
1
2
Inherited
Cost reduction coming from innovation developped on previous WTG series
Power
Cost reduction due to increase in WTG power rating
Comparison to WF with 4 MW WTG – site type A – FID 2014

## Slide 17: Offshore wind innovation to 2030
3.1 Summary & conclusions
1
3
2
Inherited
Cost reduction coming from innovation developped on previous WTG series
Power
Cost reduction due to increase in WTG power rating
New
Cost reduction due to impact of innovation on the specific WTG
Comparison to WF with 4 MW WTG – site type A – FID 2014

## Slide 18: Offshore wind innovation to 2030
Hot topics:
• Turbines with a higher rated capacity and more efficient rotors that are more reliable and deliver increased energy production
• Mass-produced support structures for use in deeper water
• Enhanced construction and OMS methods using bespoke vessels and equipment which can operate in a wider range of conditions, and
• Greater upfront investment in wind farm development, both in terms of site investigations and engineering studies.
3.2 Summary and conclusions
These hot topics show how the industry is maturing in its approach to innovation.
Game-changing innovations could reduce the cost of energy further if they can incorporate lessons from conventional offshore wind and use the current supply chain.

## Slide 19: Thank you Any questions?
Find out more www.kic-innoenergy.com
facebook.com/kicinnoenergy
twitter.com/KICInnoEnergy
linkedin.com/company/kic-innoenergy
youtube.com/user/InnoEnergy