## Slide 1: Validation of LIDAR measurements in extremely complex terrain
Wind Europe Summit
September 2016
Notes: Good afternoon again.
I am going to present now in more detail the Iberdrola study about validation of LIDAR measurements in extremely complex terrain.
The complete paper is also available, with all information and obtained results detailed.

## Slide 2: Validation of LIDAR measurements in extremely complex terrain
Introduction
Complex terrain, LIDAR and CFD models
Model parametrization and results
Results I: Data availability
Results II: Wind Speed (Mean)
Results III: Wind Speed (Maximum and distribution)
Results IV: Turbulence intensity
Conclusions
Notes: In the agenda of this presentation I am going to explain a brief introduction to the work.
Then two sections related with LIDAR in complex terrain and required dynamic correction factors.
Afterwards, in the next four sections the validation results will be summarized
And finally I will highlight the most relevant conclusions of this work.

## Slide 3: 1. Introduction
Notes: So, beginning with the introduction…

## Slide 4: 1. Introduction
An overview…
AIM
METHOD
SITE
To analyze the use of ground base continuous wave LIDAR (Zephir 300) in very complex sites.
Comparison of variables as mean wind speed or turbulence intensity measured in the LIDAR and in a nearby met mast.
Extremely complex Spanish site with a mean altitude of 1,100 m and slopes of 30º near the LIDAR device.
Notes: So, as an overview we have to say that:
The aim of the study is…
The methodology is based on the…
The test site is an extremely complex Iberdrola operational wind farm with significant altitude and slopes near the LIDAR device.

## Slide 5
Wind farm for testing (Cantabria, North Spain)
LIDAR and meteorological mast
Slopes at site in degrees. Projected WTGs (blue points) and LIDAR position (green cross)
Relative position of LIDAR and met mast
1. Introduction
Notes: In these images we can see:
The extreme complexity of the site, with significant altitude and slopes that can reach 30º near the LIDAR position.
And the relative position of mast and LIDAR.

## Slide 6: 2. Complex terrain, LIDAR and CFD models
Notes: Now, after describing the main objectives of the study and the test site, we can review some concepts about complex terrain, LIDAR and CFD models.

## Slide 7: 2. Complex terrain, LIDAR and CFD models
PROBLEMATIC
Analysis with a CFD model
Meteodyn CFD (version 5.0.3)
Non uniform flow across the LIDAR scan cone
Breakdown of the model
assumptions
Different measurements of LIDAR and CUPS
Error depends on the curvature of the flow
SOLUTION
Notes: So just to mention the well known problems of the use of LIDAR in complex terrains…
Non uniform…produces..
That leads to a…
And also…
So the final error…
And the solution applied in the present work was:
In particular the last version of Meteodyn model
In this typical figure it is represented the flow distortion that affects the LIDAR cone of measurements.

## Slide 8: 3. Model parametrization and results
Notes: And now we can see, some concrete issues of the present work related with model parametrization and results:

## Slide 9
Sharp topography in main directions needs a precise CFD model parametrization.
Dynamics correction factors by wind direction sector (10º) for each LIDAR measurement height.
Wind rose measured at site (green) and slopes at a 50 m radius from LIDAR position (orange)
Directional correction factors at different heights (36 sectors from 20 to 200m)
3. Model parametrization and results
Notes: FIRST, THE PRESENCE OF sharp topography…
The Meteodyn CFD model parametrizations are detailed in the paper.
SO, RUNNING THE MODEL INTERNALLY we obtained THE dynamics…
Very related with slopes at site as you can see

## Slide 10: 4. Results I: Data availability
Notes: Now, as we have said before, in next sections I am going to summarize the main results of the validation, beginning with data availability:

## Slide 11
Data availability (filtered by LIDAR´s internal processor) showed a significant decrease with height.
Low aerosol presence at high altitudes and unfavorable climatic conditions (fog and others).
Evolution of LIDAR (blue) and CUP (red) wind data availability with height
4. Results I: Data availability
LIDAR data filtered by adverse atmospheric conditions (green) and by low quality of measurements (orange)
Notes: AS A FIRST RESULT, data availability…
In this image we can see..
NOW IN A DETAILED ANALYSIS we can see the filtered data by LIDAR’s internal processor, by low quality of measurements in orange, and by climatic conditions (fog and others) in green which seems in this case to be responsible of the main data losses.

## Slide 12: 5. Results II: Wind Speed (Mean)
Notes: And to begin with results of the different variable comparisons, the ones related with mean horizontal WS:

## Slide 13
After applying calculated CFD correction factors, mean WS at 45 m hub height showed a BIAS of 0.6%.
Only WS > 2m/s were considered for the analysis.
BIAS was reduced in almost 10% using the calculated CFD correction factors.
LIDAR against CUP wind speeds both measured at 45m level
5. Results II: Wind Speed (Mean)
Notes: An for this analysis we applied the previously calculated CFD correction factors and mean WS BIAS…
It is important to mention that only…due to high turbulence present at low wind speeds.
And the important result in this case is that BIAS…

## Slide 14: 6. Results III: Wind Speed (Maximum and distribution)
Notes: Other interesting results are the maximum and WS distribution results

## Slide 15
Max. WS values were not correctly reproduced by LIDAR device with LIDAR max. WS values 4m/s below the ones registered by CUPs.
LIDAR and CUP WS distribution presented considerable differences in significant wind speed bins.
6. Results III: Wind Speed (Maximum and distribution)
Notes: In this case, none of them were correctly reproduced by LIDAR device.
LIDAR maximum WS values were about 4 m/s lower than the ones measured at mast.
And LIDAR and mast WS distributions had important differences in the central interval, which implies significant differences in AEP results.

## Slide 16: 7. Results IV: Turbulence intensity
Notes: And finally, TI results…

## Slide 17: Results IV: Turbulence intensity results
Directional analysis in order to validate LIDAR TI measurements: northern and southern directions were characterized separately.
Correlation of LIDAR and CUP turbulence intensity considering southern directions (135-225º).
Correlation of LIDAR and CUP turbulence intensity considering northern directions (315-45º).
Notes: …in where a directional analysis was found to be crucial at such a complex site, with important differences depending on the analyzed wind directions.
In this images we can see the TI correlation for south directions and for north directions in where TI values were higher.
And finally the tabular results, with a significantly higher BIAS in these north directions with higher TI values, while south directions where reasonable well reproduced.

## Slide 18: Results IV: Turbulence intensity results
However deviations in TI global mean values were high.
TI analysis by wind speed bins showed differences that could be crucial for site assessment purposes.
Notes: BUT EVEN THOUGH the directional analysis was reasonable, when analyzing TI global mean values, deviations were high.
AND ALSO, the analysis of TI by wind speed bins showed important differences crucial for Site Assessment purposes, AS WE CAN SEE IN THE FIGURE

## Slide 19: 8. Conclusions
Notes: And finally I would like to highlight the most relevant conclusions

## Slide 20: 8. Conclusions
At an extremely complex site…
A correct set of dynamic correction factors can reduced mean WS BIAS in an almost 10%
Significant decrease in LIDAR data availability with height
Variables as TI shall be analyzed directionally
Significant deviations of Site Assessment variables as TI and Max. WS
Non uniform flow along the LIDAR scan cone
Low aerosol presence at such altitude and unfavorable climatic conditions at site (fog and others)
Directional behaviour
Focus on Site Assessment
Notes: At such extremely complex sites…
Non uniform…REQUIRES A correct set…
HARSH CLIMATIC CONDITIONS…PRODUCE a significant…
DUE TO THE directional behavior of the flow at complex sites, variables as TI…
THE STUDY WAS FOCUSED ALSO ON SITE ASSESSMENT…AND significant deviations in the analysis of crucial variables were found, so the validity of LIDAR for site assessment purposes in this extremely complex site could not be confirmed.

## Slide 21: For more information:
Iberdrola Engineering Wind Resource Department
September 2015
sssl@iberdrola.es
Notes: This is the end of my presentation, and if you have any doubts or questions you can use mi mail or I will try my best to explain it hereafter.