## Slide 1
3-D Time-Accurate CFD Simulations of a Multi-MegaWatt Slender Bladed HAWT under Yawed Flow Conditions
Mohamed A. Sayed
PhD-Candidate
Institute of Aerodynamics and Gas-dynamics
University of Stuttgart
29.09.2016

## Slide 2
CONTENTS
Introduction and Motivation
Methodology
Effects on Wind Turbine Power
Effects on Blade Loads
Effects of Wind speed on Blade Loads
BEM-Based Comparison
Conclusion & Future Work
Notes: 2
2

## Slide 3
1. INTRODUCTION
Motivation
Currently, the size of wind turbines has increased dramatically.
The aim of the continuous research in the wind energy field is making it cheaper and more competitive.
The most important design trend has been upscaling.
Upscaling is used in order to reduce the ratio between turbine costs and produced energy.
Notes: 3
3

## Slide 4
1. INTRODUCTION
Motivation
Upscaling leads to:
Larger rotor diameter and some other structural components.
More flexible and lower stiffness blades.
More undesired vibrations or destructive flutter risk.
Increased demand to better prediction of the unsteady aerodynamic loads at the different operating conditions.
Proving that the engineering models such as BEM is still good choice for predicting the aerodynamic loads and the turbine performance.
The aim of this work
  To investigate the effect of the yawed inflow conditions on the wind turbine performance.
  To utilize the accuracy of the BEM method predicting the performance of such large turbine in comparison to CFD.
Notes: 4
4

## Slide 5
CONTENTS
Introduction and Motivation
Methodology
Effects on Wind Turbine Power
Effects on Blade Loads
Effects of Wind speed on Blade Loads
BEM-Based Comparison
Conclusion & Future Work
Notes: 5
5

## Slide 6
2. Methodology
Wind Turbine configuration
The European InnWind project designed by DTU
Rotor Diameter: 178.3 m
Hub height:119 m
FFA-W3-xxx airfoil series
Tilt angle: 5
Cone angle: -2.5 
Pre-bended blades
Wedge shaped Gurney flaps
Notes: 6
6

## Slide 7
CAD Model Generation
Grids Generation
Assembling Final CFD model
2. Methodology
Process Chain for Wind Turbine Simulations
CFD solver: FLOWer
  It is provided by the German Aerospace Center DLR with specific extensions implemented at the IAG.
Notes: 7
7

## Slide 8
2. Methodology
Computational Domain
Grid generator: Gridgen®
A structured overset mesh technique is used
Every component was meshed separately
CHIMERA overlapping mesh technique is used
Notes: 8
8

## Slide 9
2. Methodology
Tower : 1.15
Nacelle : 1.75
Hub : 2.2
Blade : 6.5
Process Chain for Wind Turbine Simulations
The grid statistics of the different domains used in the simulations are as shown in million
Notes: 9
9

## Slide 10
2. Methodology
Computational Setup
Total number of cells :  31 million
No-slip boundary conditions at the wall
y+ ≤ 1
The time-step was equivalent to 3 azimuthal-step
Wilcox k- turbulence model
448 cores were used on Cray XE6 (HLRS) named HORNET at Stuttgart University
Simulation Cases
Eight different yaw angles (60 , 45 , 30 , 15 , -15 , -30 , -45  and -60 )
Three wind speeds (7 m/sec, 11 m/sec and 15 m/sec)
Wind Speed | 7 | 11 | 15
RPM | 6 | 8.837 | 9.6
Notes: 10
10

## Slide 11
CONTENTS
Introduction and Motivation
Methodology
Effects on Wind Turbine Power
Effects on Blade Loads
Effects of Wind speed on Blade Loads
BEM-Based Comparison
Conclusion & Future Work
Notes: 11
11

## Slide 12
3. Effects on Wind Turbine Power
The presented values are normalized by the results for zero yaw angle (Baseline).
Slight increase (4%) in the Cp at ±15
Sudden decrease ( 70%) at ±60 for the wind speeds of 7 m/sec and 11 m/sec
Severe reduction is predicted in case of 15 m/sec
  CFD simulations were performed without controller, i.e constant RPM and pitch angle
  Negative blade forces in the advancing half of the rotor as a result of geometrical tilt, precone, twist angle and yaw angle.
Notes: 12
12

## Slide 13
3. Effects on Wind Turbine Power
It was suggested in the literature that the power is reduced by yawed inflow by a cosine-cubed factor and the thrust is reduced by a cosine-squared factor:
7 m/sec
15 m/sec
11 m/sec
Notes: 13
13

## Slide 14
3. Effects on Wind Turbine Power
Power oscillation amplitude is sensitive to the yaw angle
7 m/sec
11 m/sec
15 m/sec
Notes: 14
14

## Slide 15
CONTENTS
Introduction and Motivation
Methodology
Effects on Wind Turbine Power
Effects on Blade Loads
Effects of Wind speed on Blade Loads
BEM-Based Comparison
Conclusion & Future Work
Notes: 15
15

## Slide 16
4. Effects on Blade Loads
Blade loads at a Wind speed of 7 m/sec
Notes: 16
16

## Slide 17
4. Effects on Blade Loads
Blade loads at a Wind speed of 11 m/sec
Notes: 17
17

## Slide 18
4. Effects on Blade Loads
Blade loads at a Wind speed of 15 m/sec
Notes: 18
18

## Slide 19
CONTENTS
Introduction and Motivation
Methodology
Effects on Wind Turbine Power
Effects on Blade Loads
Effects of Wind speed on Blade Loads
BEM-Based Comparison
Conclusion & Future Work
Notes: 19
19

## Slide 20
5. Effects of Wind speed on Blade Loads
Zero yaw
30 yaw
60 yaw
Load distribution over one revolution normalized by the mean value over the blade radius at every wind speed
Same load At below rated wind speeds of 7 m/sec and 11 m/sec
Strong tower influence at 15 m/sec
Notes: 20
20

## Slide 21
CONTENTS
Introduction and Motivation
Methodology
Effects on Wind Turbine Power
Effects on Blade Loads
Effects of Wind speed on Blade Loads
BEM-Based Comparison
Conclusion & Future Work
Notes: 21
21

## Slide 22
6. BEM-Based Comparison
Only one wind speed 11 m/sec
2D-Polars of the FFA-W3-xxx profiles
3D-corrections and Polar extrapolation
Blended profiles
Notes: 22
22

## Slide 23
6. BEM-Based Comparison
FFA-W3-241
Notes: 23
23

## Slide 24
6. BEM-Based Comparison
AeroDyn v13 (SIMPACK integrated module)
39 Elements
16 Profiles Polar (Blended profiles included)
No Tower shadow
BEDDOES Dynamic stall
Prandtl tip- and hub-loss
Equilibrium Inflow
Swirl Induction-factor
Notes: 24
24

## Slide 25
6. BEM-Based Comparison
7% difference predicted
Symmetric distribution
Unable to predict correctly the behavior at small yaw angles
Cosine rule fail but BEM followed
Notes: 25
25

## Slide 26
CONTENTS
Introduction and Motivation
Methodology
Effects on Wind Turbine Power
Effects on Blade Loads
Effects of Wind speed on Blade Loads
BEM-Based Comparison
Conclusion & Future Work
Notes: 26
26

## Slide 27
8. Conclusion & Future Work
Conclusion
CFD simulations of a yawed large slender bladed HAWT were conducted using a 3D URANS flow solver based on structured overlapped meshes
Different yawed conditions have been examined ranging from +60 to -60
For small yaw angles below ±15, the aerodynamic loads over the blades are slightly increased
For higher yaw angles above ±15 the aerodynamic loads are significantly reduced
Larger load fluctuations were predicted as the yaw angles were increased
At wind speeds less than rated wind speed, the yaw angle is the most dominating factor affecting the blade load distributions over one revolution more than the wind speed
At above rated wind speed of 15 m/sec, the wind speed has an utmost effect on the load distributions over one revolution
For the investigated conditions, BEM underestimated the power results and predicting symmetric behavior for the yaw angles
Notes: 27

## Slide 28
8. Conclusion & Future Work
Future work
Improving the BEM results
Including Tower shadow in BEM
Utilizing above rated wind speed with BEM
Aero-elastic simulations
Notes: 28

## Slide 29
Thank You for Your Attention
Questions?
sayed@iag.uni-stuttgart.de
Notes: 29