## Slide 1: Scanning LiDAR in Offshore Wind
Field testing scanning LiDAR systems in Dublin Bay
Michael Stephenson and Alex Clerc
Wind Europe Summit, 27th September 2016
Co-authors:
Peter Stuart, Lee Cameron, Alina Burmester, Simon Feeney (RES)
Matthieu Boquet, Philippe Royer, Raghavendra Krishna Murthy (Leosphere)
Keith Barr (Lockheed Martin Coherent Technologies - LMCT)

## Slide 2: Presentation Contents
Project Description
  Value proposition
  Single vs Dual Scanning LiDAR
  Dublin Bay experiment
Project Results
  Radial, single LiDAR and dual LiDAR validation results
  Leosphere and LMCT
Project Conclusions

## Slide 3: What are we trying to achieve?
  The benefits that could be derived from installing Scanning LIDAR(s) include:
    Better project decisions (layout design, resource assessment)
    Reduction in horizontal wind speed extrapolation uncertainty
  In this experiment primary wind speed measurement (e.g. as done by a mast or floating LiDAR) is a secondary objective. Scanning patterns are optimised for spatial variation.
~1% change in wind speed
~20km
Predicted spatial variation of average wind speed (mesoscale model)
~1% change in wind speed
~1% change in wind speed

## Slide 4: Definition of Radial and Orthogonal Measurement Data
Wind vector
Measured radial wind speed
East Pier
Kish Lighthouse
Line of Sight (LOS)
Scanning LiDAR
Measurement
Location

## Slide 5: Definition of Radial and Orthogonal Measurement Data
Wind vector
Measured radial wind speed
East Pier
Kish Lighthouse
Notes: Wind vector changed 45 degree

## Slide 6: Definition of Radial and Orthogonal Measurement Data
Wind vector
Measured radial wind speed = 0m/s
East Pier
Kish Lighthouse
… but wind direction can be measured very accurately
Notes: Wind vector changed 45 degree

## Slide 7: Wind direction considerations
East Pier
Kish Lighthouse
Across LOS
Along LOS
Along LOS
Across LOS
LOS = Line Of Sight
Notes: Wind vector changed 45 degree

## Slide 8: Scanning LiDAR
Single LiDAR Measurement:
  Wind speed and direction calculation based on multiple measurements along an arc
  Homogenous flow is a key assumption
Dual LiDAR Measurement
  Wind speed and direction calculation based on measurement of two devices
  Wind vector can be accurately determined without assuming homogenous flow
  BUT higher cost, higher risk of data loss, etc.
Scanning LiDAR
Scanning LiDAR
Scanning LiDAR
Measurement Location
Measurement Location

## Slide 9: Campaign Overview
East Pier
Scanning LiDAR
Baily Lighthouse
400s
Prototype
Notes: Time of measurement start end date

## Slide 10: Measurement Location Overview
Baily Lighthouse
Poolbeg
East Pier
Kish Lighthouse
Scanning LiDAR
Validation LiDAR
Notes: Time of measurement start end date

## Slide 11: Demonstration Points
Demonstration Points
Validation LiDAR
Poolbeg
East Pier
Kish Lighthouse
Scanning LiDAR
Baily Lighthouse
Notes: Measuring points agreed with both manufacturers

## Slide 12: Demonstration Points
Demonstration Points
Validation LiDAR
Poolbeg
East Pier
Kish Lighthouse
Scanning LiDAR
Baily Lighthouse
~10km
Notes: Measuring points agreed with both manufacturers

## Slide 13: The Validation set up
Scanning LiDAR
Validation Point (Windcube vertical LiDAR)
Kish Lighthouse (30m tall structure) is dot in distance, Windcube Vertical LiDAR on top
100m
150m

## Slide 14: Campaign Details
~4 months of concurrent measurements from all devices
Furthest demonstration point: 15km.
Scan pattern designed by OEMs.
  Leosphere: dual RHI at Poolbeg, PPI at all other points
    integration time 400s = 1 second, scan rate = 3deg/s PPI, 0.1deg/s RHI
    integration time Prototype = 0.5 second, scan rate = 6deg/s PPI, 0.1deg/s RHI
  LMCT: PPI at all points. integration time = 1 second, scan rate <= 2.5deg/s
Pictures courtesy of Leosphere

## Slide 15: Campaign Details
Hard targets used (Kish lighthouse, Poolbeg towers) to calibrate and verify beam pointing accuracy

## Slide 16: Campaign Details
Hard targets used (Kish lighthouse, Poolbeg towers) to calibrate and verify beam pointing accuracy
Pictures courtesy of Leosphere

## Slide 17: Achieved measurement ranges
WindTracer: 70% data coverage at 14km for Baily device
Pictures courtesy of LMCT

## Slide 18: Achieved measurement ranges
WindTracer : 70% data coverage at 14km for Baily device
Leosphere:
  70% data coverage at 9km for 400s and 11km for Prototype
Windcube 400S: ~60% data availability at Kish (10.2km distance)
92.3% uptime.
Prototype: ~50% data availability at Kish (13.4km distance).
97.5% uptime.
Graph courtesy of Leosphere

## Slide 19: WindTracer results
Radial results: technology works – radial measurements highly precise and accurate
Single LiDAR results: flow inhomogeneity impacts precision and accuracy
Dual LiDAR results: full vector measured precisely and accurately
Dual LiDAR
Single LiDAR
Radial
slope = 0.97
11k points
slope = 0.95
11k points
slope = 0.99
4k points

## Slide 20: Leosphere results
Radial results: technology works – radial measurements highly accurate
Single LiDAR results: flow inhomogeneity impacts precision and accuracy
Dual LiDAR results: better accuracy but similar precision as Single
Dual LiDAR
Single LiDAR
Radial
slope = 0.99
5k points
slope = 0.93
8k points
slope = 0.99
3k points

## Slide 21: Leosphere results
Alternatively processed dual results: similar accuracy and better r2, but lower data count
Compromise between data count and precision
Note this is a blind comparison; OEMs now have access to the validation data to improve their algorithms
Dual LiDAR
Single LiDAR
Radial
slope = 0.99
5k points
slope = 0.93
8k points
slope = 1.00
2k points

## Slide 22: Validation Summary
For both devices, the single LiDAR accuracy is insufficient for measuring spatial variation for the distances considered in this project (5km-15km)
Dual LiDAR configuration gives very accurate speed up measurements
Note validation performed blind and scan patterns were designed to measure at 12 points evenly (not focused on any particular point)
 | LOS WS | Single LiDAR | Dual LiDAR
Number of Validations | 10 | 10 | 4
Average R2 | 0.994 | 0.846 | 0.983
Maximum Speed Up Error | 2.6% | 13.6% | 1.1%
LMCT WindTracer
 | LOS WS | Single LiDAR | Dual LiDAR
Number of Validations | 4 | 6 | 4
Average R2 | 0.982 | 0.853 | 0.889
Maximum Speed Up Error | 2.3% | 16.6% | 3.7%
Windcube 400S/Prototype

## Slide 23: Impact on Yield Prediction Uncertainty
The observed speed up errors using dual LiDAR systems are < 2%
This represents an improvement in uncertainty in spatial variation of wind resource relative to current standard methods (mesoscale modelling)
A conservative estimate suggests dual scanning LiDAR measurements of spatial variation can reduce yield prediction uncertainty by 0.1% - 0.4% for a near shore site like Dublin Bay
Single LiDAR errors are too high at Dublin Bay to reduce uncertainty, likely due to flow inhomogeneity
Uncertainty Term | Without Scanning LiDAR | With Scanning LiDAR
Long Term WS Uncertainty | 3.9% | 3.9%
Other (Wakes, Power Curve, etc.) | 5.4% | 5.4%
Spatial | 2.5% | 1.3%
Total Uncertainty | 7.1% | 6.8%
P90/P50 | 90.9% | 91.3%

## Slide 24: Conclusions
High accuracy measurements validated in a unique experiment
For long measurement ranges dual LiDAR has a substantial accuracy and precision benefit over single LiDAR
For this theoretical wind farm a Scanning LiDAR campaign would
  Reduce the yield uncertainty and therefore investment risk
  Facilitate better project decisions (eg turbine layout)

## Slide 25: Thank you
Thank you to Commissioners of Irish Lights, Carbon Trust, the Offshore Wind Accelerator, Leosphere, LMCT, and RES!
Public paper with further details to follow – please contact Carbon Trust for more information
Dublin Bay is an active test site – please contact RES for more information

## Slide 27: Validation Sensitivity Analysis
Single LiDAR results: high errors apparent for wind directions orthogonal to LOS
Dual LiDAR results: reduction in sensitivity of accuracy to wind direction
LOS East Pier
LOS East Pier
Single LiDAR
Dual LiDAR
EP
Baily
EP
Baily