## Slide 1: Spatial Modeling Performance in Complex Terrain Scott Eichelberger, Vaisala

## Slide 2: What is in our head…

## Slide 3: What is in our head…
Linearized Flow Model
Flow = mean + perturbation
Sheltering Obstructions
Surface Roughness
Terrain Variability

## Slide 4: Complex Terrain Expectations
Over-predict when moving downhill

## Slide 5: Complex Terrain Expectations
Over-predict when moving downhill
Under-predict when moving uphill

## Slide 6: Complex Terrain Expectations
Over-predict when moving downhill
Under-predict when moving uphill
Based on these expected errors, best practice is to bracket
the wind resource with measurements

## Slide 7: Using High Performance Computing to run Numerical Weather Prediction Models

## Slide 8: Using High Performance Computing to run Numerical Weather Prediction Models

## Slide 9: NWP Model Setup
WRF Version 3.5.1
Nested grids: 40.5km, 13.5km, 4.5km, 1.5km, and 500m
Reanalysis data: MERRA
Terrain data: SRTM 90m
Landuse data: GlobCover 300m
Time-Varying Microscale Model to final 90m resolution

## Slide 10: NWP Model Setup
4.5km resolution
1.5km resolution
500m resolution

## Slide 11: NWP Model Setup
4.5km resolution
1.5km resolution
500m resolution
90m resolution
All modeling done in the time domain – preserving the weather pattern variability

## Slide 12: Site Description
Domain Size (25km x 35km)
15 met towers
80m top anemometer height
~2 years of overlapping data across towers
Max 1.6 m/s difference between wind speeds at met towers
Max 265m difference between elevations at met towers

## Slide 13: Site Description
Domain Size (25km x 35km)
15 met towers
80m top anemometer height
~2 years of overlapping data across towers
Max 1.6 m/s difference between wind speeds at met towers
Max 265m difference between elevations at met towers
Almost no correlation between elevation and mean wind speed values

## Slide 14: Wind Speed vs Elevation
Upstream topography blocks wind flow upsetting typical relationship

## Slide 15: Round Robin Validation
Raw model results are calibrated using a single met tower

## Slide 16: Round Robin Validation
Raw model results are calibrated using a single met tower
Spatial validation is tested by comparing the calibrated data to the observed data at the remaining met towers

## Slide 17: Round Robin Validation
Raw model results are calibrated using a single met tower
Spatial validation is tested by comparing the calibrated data to the observed data at the remaining met towers
Process is repeated for each individual met tower

## Slide 18: Round Robin Validation
Statistics | 
n | 210
Observed RMSE | 5.5%
Theory RMSE | 5.7%
A systematic method for quantifying flow model uncertainty in wind resource assessment – Alex Clerc et al.

## Slide 19: Elevation Delta vs Error
Mesoscale modeling results show no significant
relationship between elevation delta and error

## Slide 20: Wind Speed Delta vs Error
Mesoscale modeling results show no significant
relationship between wind speed delta and error

## Slide 21: Geographic distribution of bias
Chart: 
| -42.646470000000001 | -42.636340000000011 | -42.641509999999997 | -42.53539 | -42.65081 | -42.611759999999997 | -42.603859999999997 | -42.558230000000002 | -42.637909999999998 | -42.681249999999999 | -42.635020000000011 | -42.636609999999997 | -42.70176 | -42.610909999999997 | -42.611629999999998
 | -14.1829 | -14.003 | -13.9522 | -14.115 | -14.1066 | -14.1017 | -14.1273 | -14.1255 | -13.9635 | -14.0724 | -14.0046 | -13.9881 | -14.1236 | -14.0855 | -14.1121
 | Weighted Mast Prediction Error (%) | Nearest Mast Prediction Error (%) |  | Weighted Predictive Distance (km) | Nearest Predictive Distance (km)
M1 | 1.4% | -2.3% |  | 14.40 | 8.52
M2 | -4.1% | 5.2% |  | 10.30 | 0.91
M3 | 0.8% | 1.1% |  | 13.45 | 1.53
M4 | 7.4% | 4.5% |  | 13.40 | 3.97
M5 | 4.4% | 9.0% |  | 11.25 | 5.14
M6 | 1.7% | -0.9% |  | 8.84 | 1.63
M7 | 6.1% | -0.9% |  | 9.79 | 1.95
M8 | -3.4% | -4.6% |  | 11.32 | 3.97
M9 | 1.5% | 2.0% |  | 12.67 | 1.53
M10 | -6.7% | -2.3% |  | 11.78 | 5.14
M11 | -3.0% | 6.2% |  | 9.57 | 0.91
M12 | -2.0% | 6.2% |  | 10.58 | 1.65
M13 | -2.4% | -2.3% |  | 13.64 | 5.82
M14 | 0.5% | 0.0% |  | 9.20 | 3.21
M15 | 2.5% | 0.0% |  | 8.30 | 1.63
RMSE | 3.8% | 4.1% | Average | 11.23 | 3.17
Bias | 0.3% | 1.4% |  |  | 

## Slide 22: Geographic distribution of bias
 | Weighted Mast Prediction Error (%) | Nearest Mast Prediction Error (%) |  | Weighted Predictive Distance (km) | Nearest Predictive Distance (km)
M1 | 1.4% | -2.3% |  | 14.40 | 8.52
M2 | -4.1% | 5.2% |  | 10.30 | 0.91
M3 | 0.8% | 1.1% |  | 13.45 | 1.53
M4 | 7.4% | 4.5% |  | 13.40 | 3.97
M5 | 4.4% | 9.0% |  | 11.25 | 5.14
M6 | 1.7% | -0.9% |  | 8.84 | 1.63
M7 | 6.1% | -0.9% |  | 9.79 | 1.95
M8 | -3.4% | -4.6% |  | 11.32 | 3.97
M9 | 1.5% | 2.0% |  | 12.67 | 1.53
M10 | -6.7% | -2.3% |  | 11.78 | 5.14
M11 | -3.0% | 6.2% |  | 9.57 | 0.91
M12 | -2.0% | 6.2% |  | 10.58 | 1.65
M13 | -2.4% | -2.3% |  | 13.64 | 5.82
M14 | 0.5% | 0.0% |  | 9.20 | 3.21
M15 | 2.5% | 0.0% |  | 8.30 | 1.63
RMSE | 3.8% | 4.1% | Average | 11.23 | 3.17
Bias | 0.3% | 1.4% |  |  | 
Weighted mast predictions show much better error characteristics than using the nearest mast only, despite the average predictive distance being substantially higher.

## Slide 23: What does this mean?
You can have “reasonable” predictive uncertainties at distances of >10 km
One should distribute measurements in a way that looks for mesoscale wind regime features, not necessarily bracketing the resource
Mesoscale models and a good measurement campaign can be leveraged to significantly improve spatial modeling uncertainty – even in complex terrain

## Slide 24: Thank you
Scott Eichelberger
scott.eichelberger@vaisala.com