## Slide 1: Validation of remote sensing methods for ice detection
WindEurope 2016 Timo Karlsson, VTT
Notes: You can use cover page with one or two photos or without photos

## Slide 2: Authors
Timo Karlsson, Ville Lehtomäki, VTT
Juha Paldanius, Vaisala
Jaakko Kleemola, Suomen Hyötytuuli
Martin S. Grønsleth, Kjeller Vindteknikk
Zouhair Khadiri-Yazami, Fraunhofer IWES

## Slide 3: Icing and wind power
Ice accretion on turbine blades reduces output power of the turbine
Falling ice is a health and safety risk
Cold climate wind is a substantial market
Cumulative installed capacity by end of 2015 [MW] |  | Forecasted capacity by end of 2020 [MW] | 
Low temperature | Icing | Low temperature | Icing
40 500 | 86 500 | 62 500 | 123 000
Total 127 000 |  | Total 185 500 | 
Source: V. Lehtomäki, Emerging from the cold, Wind Power Monthly, 29.7. 2016 , http://www.windpowermonthly.com/article/1403504/emerging-cold

## Slide 4: Icing types
Icing needs liquid water & freezing temperature
Low level clouds & T<0°C = in-cloud icing (most typical)
*Source: IEA Wind Task 19 Available Technologies report of Wind Energy in Cold Climates
(2016 edition): http://www.ieawind.org/task_19.html

## Slide 5: IEA Ice Classification¹
IEA Ice Class | Duration of Meteorological Icing [% of Year] | Duration of Instrumental Icing [% of Year] | Production Loss [% of AEP]
5 | >10 | >20 | >20
4 | 5-10 | 10-30 | 10-25
3 | 3-5 | 6-15 | 3-12
2 | 0.5-3 | 1-9 | 0.5-5
1 | 0-0.5 | <1.5 | 0-0.5
¹: IEA Wind Recommended Practices for wind energy projects in cold climates edition 2011

## Slide 6: Remote ice detection
Use a LIDAR or ceilometer to determine cloud base height
Combine with meteorological measurements to produce warnings of meteorological icing
Measure icing at almost any height with ground based instrument
Create an icing profile for the measurement location
US Patent 2014/0192356
  Arrangement and method for icing detection
    Esa Peltola, Petteri Antikainen, Andrea Vignaroli

## Slide 7: Method principle
Lidar measures wind speeds with laser
Light reflected back from particles in air
Cloud->more particles in air-> stronger backscatter signal
Ceilometer Based on same priciple
Ceilometer only measures cloud cover height, not wind speed
Measurement signal
Backscatter signal

## Slide 8: Sites
Site | Country | Instrumentation | Time period
Site A | Finland | Vaisala CL31 ceilometer Wind turbine heated/non-heated anemometers [100 m agl] | Dec 2015-Apr 2016
Site B | Germany | Leosphere WindCube LIDAR Jenoptik/Lufft CHM 15K ceilometer Heated/nonheated anemometers [190 m agl] Webcam | Oct 2012 –Feb 2014
Site C | Norway | Leosphere WindCube LIDAR Combitech IceMonitor ice detector [90 m agl] webcam | Jan 2012- Jun 2014
Site D | Finland | Leosphere WindCube LIDAR Vaisala CL31 Ceilometer | Fed 2016-Jun 2016

## Slide 9: Data overview

## Slide 10: Data overview

## Slide 11: Conditions during icing
Instrumental icing most common at
  temperatures close to 0 °C
  Wind speed < 10 m/s
Site A
Site B
Site C

## Slide 12: Correlation
Correlation between meteorological and instrumental icing measurements
Calulated for different time windows for all sites
Shows that correlation starts to improve only when observation window is long
Chart: Correlation Coefficient
| 0.04 | 0.125 | 0.25 | 0.5 | 1 | 5 | 10 | 15 | 30
Site B | 0.11847 | 0.1298 | 0.15039 | 0.16398 | 0.25125 | 0.46971 | 0.53713 | 0.69652 | 0.93572
Site C | 0.07712 | 0.11361 | 0.15545 | 0.21833 | 0.27429 | 0.48249 | 0.62367 | 0.62765 | 0.77127
Site A | 0.04564 | 0.05248 | 0.06439 | 0.07582 | 0.09788 | 0.3519 | 0.66631 | 0.90064 | 0.89984

## Slide 13: Site Classification
Ice classification hits same class at site B
Site C way under
  Availability also very low
  From ice sensor meteorological icing
    4.4 %/class 3
Ice class requires at least a year of data
Site | Meteorological icing from Ceilometer [% of time] | Meteorological icing from wind LIDAR [% of time] | Instrumental icing [% of time]
Site A | 5 %: | - | 11.2 %:
Site B | 3 %: Class 2 (Ceilometer) | 1.8 %: Class 2 (LIDAR) | 3.8 %: Class 2
Site C | - | 2 %: Class 2 | 14.9 %: Class 3
Site D | 1.6 %: | 2.0 %: | -

## Slide 14: Conclusions and future work
Remote sensing of icing looks promising
Availability an issue when using LIDAR
  Better during icing than on average. Might still miss events.
Ceilometer no availability issues, also resolution better
Correlation on a longer timescale
  Can give an estimate of conditions
  No real time detection
Improve LIDAR data availability
Cloud composition
  Water vapor / ice crystals
Now compares Meteorological icing to instrumental icing
  Different reference needed
  Better transfer from meteorological to instrumental icing