## Slide 1
TetraSpar
A New Floating Concept
Henrik Stiesdal, 29 September, 2016

## Slide 2
In-Float Concept, 2015
Keep it simple!
Tetrahedral structure with minimal bending moments
Modular – all components manufactured in factories, no fabrication in harbor
Components with dimensions and weights known from wind turbines, transported by road
Components assembled with bolts
Buoyancy with pressurized tanks – lightweight structures with no need for dimensioning to hydrostatic pressure

## Slide 3
Onshore wind reference for concept
Onshore wind industry
Proven track record in continuous improvement and cost reductions
Currently offers lowest cost new capacity, Cost of Energy range $30 - $100 per MWh, competing favorably with coal, gas, nuclear
Basis for low cost and high efficiency
Standardization and modularization
Industrialized manufacturing, components all factory-made, no fabrication on site
Road or rail transportation of limited number (6-10) of main modules
Main modules assembled on site by bolting
Installation of 500-ton structure in few days
Picture credit: Siemens

## Slide 4
The In-Float Concept
Cast TP, classical wind turbine hub technology
Tapered, welded center column, classical wind turbine tower technology
Cylindrical, welded braces, classical wind turbine tower technology
Steel or GRP tanks, classical industrial technology
Cast nodes, classical wind turbine hub technology

## Slide 5
Two levels of innovation in In-Float concept
Level 1 – Technical
New structural and installation concept with industrialization as key focus
Level 2 – Dissemination
Open source arrangement with royalty-free license to IP offered to any interested party
Consequence of Open source arrangement
Generous offer by DNV-GL to review design concept free of charge

## Slide 6
Result of DNV GL Effort – In-Float Concept Feasibility Evaluation
Conclusion from Evaluation Report
“At the present stage of development, DNV GL has not identified any unsolvable development barriers and thus believes the concept is well suited for further conceptual development”.
Source: DNV GL

## Slide 7
Observations regarding reception of In-Float Concept
Academia, small companies, consultants, small suppliers
Great interest
Many offers for collaboration, supplier engagement, etc.
Other floater developers and large substructure suppliers
Low interest – too much capital (real and emotional) invested already
Large developers
Great interest, but always with the caveat – “Well, open source … we would much have preferred if we could have it as an exclusive … we need some sort of entrepreneurial ownership … come back with something that we can have to ourselves!”
So – a supplementary solution needed that can be licensed and provide exclusivity for specific geographical areas or use cases

## Slide 8
Enter the TetraSpar, 2016
Picture credit: DNV GL

## Slide 9
TetraSpar Concept – In-Float with a twist
Getting the benefits of the spar
without the drawbacks
In-Float foundation with a counterweight, suspended under foundation
When deployed, counterweight ensures that center of gravity is below center of buoyancy, creating simple stability
Counterweight is made with ballasted tanks that have sufficient buoyancy when air-filled to float
IP secured by Stiesdal

## Slide 10
TetraSpar Concept

## Slide 11
TetraSpar variants at different water depths – range 10-1000 m

## Slide 12
IEA Forecast of Wind Energy Costs, 2016
Source: DoE, NREL, IEA
156
136
63
TetraSpar
50-100

## Slide 13
The money is in industrialization!
Source: Ford Motor Company

## Slide 14
The learning curve, Li-ion batteries and crystalline PV modules
Source: Bloomberg New Energy Finance

## Slide 15
Thanks for your attention
Henrik Stiesdal
hst@stiesdal.com