## Slide 1: Generation and validation of spatial distribution of hourly wind speed time-series in cold climates using Machine Learning
Stefano Grassi
WindEurope Summit 2016
28.09.2016

## Slide 2: Layout
Introduction
WRA methods
Case study
  Icing map
  Wind speed and energy production
Results and Conclusions

## Slide 3: Introduction
Wind resource assessment is fundamental when selecting a site for wind energy projects since the early stages
Two main methods are used for mesoscale maps of wind resource
  Wind flow models, mesoscale weather prediction systems
  (geo)statistical and ML methods
Source: PNE Wind

## Slide 4
Physical Wind Flow Models
Source:http://www.deskeng.com
Based on physical laws of mass and momentum conservations, or computational fluid-dynamics equations.
Input data: wind speed measurement and geomorphological data
Industry standard
Fairly accurate
Time-consuming and computationally demanding

## Slide 5
Machine learning based models
Joseph Rickert - http://blog.revolutionanalytics.com
Target variable estimated based on its correlation with environmental spatio-temporal covariates (or predictors)
  Input data: more wind speed measurements and spatial predictors required
    10’000+ predictors used
  Generally less accurate
  Fast and efficient
  Site-specific uncertainty

## Slide 6
How does the method work?
10 min measurements are resampled to obtain a distribution of likely wind speeds
Data fed into machine learning algorithm
The final output is a time-series with confidence intervals

## Slide 7: Study area: icing map
Source: Meteotest
based on raster of cloud water, temperature and wind from COSMO-2,
  input of icing algorithm simulating ice mass accretion on rotating cylindric structure
average annual number of instrumental icing below 12 days (≈ 3.2%)
153 weather stations used for WRA
Time resolution: 10min (over 5 years)

## Slide 8: Icing issues on measurements
40% weather stations: < 500m
66% weather stations: < 1000m
Wind parks located below 2000m
  Icing generates annual energy losses 0-5%

## Slide 9
Validation
5-Folds Spatio-Temporal cross-validation
20% of the data excluded from training and used to predict wind speed in a specific time window
Bias distributions (i.e. Difference between observation and estimation), aggregated by month
  Variation of bias: P95 > P5
The mean bias is:
  P95: -0.11m/s
  P5: -0.08m/s

## Slide 10
Results: wind speed profile
This method allows estimating:
Spatio-temporal distribution of the wind speed profile
  10min → hourly (or greater)
the confidence intervals of wind speed
  Wind direction included (but not presented)
Range of variation of long-term wind speed

## Slide 11
Result: wind energy production
Estimate of the long-term probabilistic hourly variability of the electricity generation
  wind direction → impact of wake effect
  Energy losses due to icing effect applied as a function of temperatures profile

## Slide 12
Conclusions
Machine learning methods provide spatio-temporal distribution of confidence intervals and measure of uncertainties.
Method applied in Switzerland characterized by alpine climate
  Icing generates average annual energy losses up to 5% in alpine regions
  Most weather stations and regions suitable for wind farms below 2000m: <10 days instrumental icing
Estimation of the wind speed variability with high temporal resolution.
  Validation shows a mean bias of -0.08m/s (P5) and -0.11m/s (P95)
Wind speed profile useful to assess scenarios of long term energy production profiles

## Slide 13
Thank you!!
http://www.gis.ethz.ch/