## Slide 1: Aerodynamic Simulation of the MARINTEK Braceless Semisubmersible Wave Tank Tests
Gordon Stewart
Post-doctoral Researcher
NTNU

## Slide 2: MARINTEK Braceless Semisubmersible
1/30th Froude scale braceless semisubmersible
Uses a scaled version of the NREL 5MW turbine
Features a novel aerodynamic actuator that consists of 6 wires that are tensioned by motors to provide aerodynamic forces, which eliminates the issue of the Reynolds/Froude scaling mismatch that occurs for scaled experiments
This actuator is controlled by a blade-element momentum theory based code that allows for real-time coupling between platform motion and the simulated aerodynamic forces
Figure courtesy of MARINTEK

## Slide 3: Aerodynamic Modeling
How to best model the aerodynamic actuator used in these experiments?
Turbsim Wind file
Aerodyn
Forces applied to Platform
Platform Motion

## Slide 4: Aerodynamic Modeling
How to best model the aerodynamic actuator used in these experiments?
Turbsim Wind file
Aerodyn
Forces applied to Platform
Platform Motion
Contained within simulation tool

## Slide 5: Aerodynamic Modeling
How to best model the aerodynamic actuator used in these experiments?
Turbsim Wind file
Aerodyn
Forces applied to Platform
Platform Motion
Bypass aero- solver, use experimental forces directly

## Slide 6: Simulation Tool
The MARINTEK data was unavailable at the time of this research, so results from a simulation only study will be presented
Uses a modified version of FAST, from NREL, that allows for the bypassing of the aerodynamics solver by reading an external file of rotor forces

## Slide 7: Description of Simulations Conducted
A set of FAST simulations at various wind speeds and wave heights were run using the OC3 spar buoy floating platform
An artificial experiment was created by running a set of baseline simulations
The rotor forces of the baseline simulation were recorded and used in place of the aerodynamic forces in a second set of simulations. For these simulations, the coefficient of drag of the platform is modified to represent modeling inaccuracies

## Slide 8: Coefficient of Drag Modification- Tower Bending Moment Standard Deviation
On the left, both sets of simulations use the baseline version of FAST with AeroDyn enabled, but using 2 different Cd values; 0.6 (the original value), and 0.5
On the right, the baseline values with the original Cd of 0.6 is compared to a set of simulations that used the aerodynamic loads from the baseline, but has a lower Cd value

## Slide 9: Phase of Loading is Important
This figure on the left shows a comparison between a baseline simulation with 4 m initial surge and a simulation that uses the aerodynamic forces from the baseline simulation, but starts with an initial surge of zero meters
The figure on the right shows a comparison of three simulations:
  baseline with initial platform pitch 5 degrees (blue solid line),
  initial pitch of -5 degrees using the aerodynamic forces from the baseline (green dashed line),
  no aerodynamic forces and initial pitch of -5 degrees (red dot-dashed line)

## Slide 10: Conclusions
Using aerodynamic forces directly from the experiment is relatively accurate as long as the hydrodynamic modeling is also accurate
However, if there are larger inaccuracies in hydrodynamic modeling, especially inaccuracies in phase or frequency in platform degrees of freedom, other methods of aerodynamic modeling may be necessary
Hybrid actuation systems like the one used in the MARINTEK experiments create many opportunities for the creation of accurate and useful experimental data, but the modeling of the aerodynamic system must be approached with care

## Slide 11: Acknowledgements
The research leading to these results has received funding from the European Union’s Seventh Framework Program (FP7/2007-2013) under grant agreement number 609795
Thanks to my colleagues at MARINTEK for their help with this work, especially Erin Bachynski, Madjid Karimirad, and Thomas Sauder
Also thanks to my supervisor, Michael Muskulus

## Slide 12: Supplemental: Coefficient of Drag Modification- Surge Standard Deviation
On the left, both sets of simulations use the baseline version of FAST with AeroDyn enabled, but using 2 different Cd values; 0.6 (the original value), and 0.5
On the right, the baseline values with the original Cd of 0.6 is compared to a set of simulations that used the aerodynamic loads from the baseline, but has a lower Cd value

## Slide 13: Supplemental: Different Wave Field- Surge Standard Deviation
In these plots, instead of modifying the Cd, a new irregular wave field is created for each simulation with the same Hs and Tp as the baseline, which represents the inability of some design codes from using a wave height time series as an input

## Slide 14: Supplemental: Different Wave Fields- Surge
These plots are selected time series from a 10 m/s mean wind speed simulation, showing the surge for the two wave seeds.
Note the similar trends in surge even with different wave inputs, due to the wind being the same and surge being dependent mostly on the thrust force

## Slide 15: Supplemental: Different Wave Field- Tower Bending Moment Standard Deviation
Here again, a new irregular wave field is created for each simulation with the same Hs and Tp as the baseline, which represents the inability of some design codes from using a wave height time series as an input

## Slide 16: Supplemental: Different Wave Fields- Tower Bending
Here, for the tower bending moment time series, the result is more wave-dominated
The comparison of the baseline with wave random seed 2 and the same wave seed with predefined aerodynamic loads (lower right) shows very similar loads due to these simulations having the same waves