## Slide 1
Innovative
Heat Storage Concept
Henrik Stiesdal, 28 September, 2016

## Slide 2
High-Temperature Thermal Energy Storage (HT-TES) addresses the growing need for reliable, cost-effective bulk energy storage
Provides high flexibility in storage capacity at low cost impact – can store huge amounts of energy for days or weeks
Addresses all relevant storage requirements
Uses proven, off-the-shelf technology
Can be configured to take advantage of brownfield recycling of retiring coal and gas plants
Can also be configured to provide new capacity at greenfield sites
Is well suited for connection to district heating systems

## Slide 3
Fundamental arrangement of HT-TES
Charge Discharge
Existing New
3
2
4
1
5
7
6
8
9
Rock bed
Charging fan
Charging heater
Discharging fan
Heat recovery steam generator
Steam turbine
Generator
Condenser
Feed pump
Cooling arrangement, e.g. district heating
10

## Slide 4
Basic principle of HT-TES - charging
When storage system is charged, hot air is circulated through rock bed

## Slide 5
Basic principle of HT-TES – discharging
When storage system is discharged, hot air is circulated from rock bed through heat recovery steam generator replacing boiler in conventional steam power plant

## Slide 6
Flexible HT-TES – Brayton Cycle
Charge system and storage unit same as for steam cycle, but operate at higher temperature (800-900 °C)
Discharge system based on gas turbine with intercooler and recuperator
Target uses: Peaker replacement, ancillary services, energy security

## Slide 7
Flexible HT-TES – CAES Variant
HT-TES can be applied in CAES variant, improving efficiency to >70% by storing compressed air.
Configuration similar to classical adiabatic CAES, but with high-efficiency thermal storage and low-cost tanks.
Target uses: Dispatchable PV, reduced grid connection capacity

## Slide 8
Storage material
All solids (metals, stone, concrete, etc.) have roughly same heat capacity.
Basalt rock has advantages of low cost and robustness to repeated heating
Energy density ~100 kWh/m3
Hazelnut / walnut dimensions of pebbles provide optimum balance between heat transfer and pressure drop

## Slide 9
15.000 MWh storage unit
Footprint 100x250 m, height 12 m
175.000 m3 of crushed basalt rock placed in U-shape to facilitate inlet and outlet at same end
1 m insulation top and bottom, 1 m earth cover
Heat loss ~0.5% per day

## Slide 10
The consequence of the discharge technology …
Discharge is through the synchronous generator of a conventional power plant
As a consequence, HT-TES can provide all types of ancillary services –
    Voltage regulation
    Frequency regulation
    Spinning reserve and inertial response
    Black start
With trickle discharge the system is always on-line, also when being charged

## Slide 11
Chart: Hours of storage
| 1 | 3 | 6 | 12 | 24 | 48 | 120 | 240
HT-TES, Rankine | 698.8277 | 266.4182 | 158.3159 | 104.2647 | 77.2391 | 79.8336 | 87.6169 | 100.5892
Li-ion | 444.0918 | 425.1739 | 420.4444 | 418.0797 | 416.8973 | 810.9109 | 1992.9515 | 3963.0193
HT-TES has significant cost advantage for longer-term storage
Charge cost $20/MWh
1 charge-discharge cycle per day
Maximum 50% DoD (Depth of Discharge)

## Slide 12
Storage costs depend on charging costs
Chart: Cost of Energy from Storage, $/MWh
| HT-TES, Rankine | HT-TES, Brayton | HT-TES, CC | H2 | Pumped hydro | Li-ion | Lead acid | VRB | Molten metal
Charge @ $0/MWh | 29.62 | 98.4528 | 49.8525 | 65.4218 | 98.8776 | 395.1959 | 408.6769 | 703.1279 | 693.1316
Charge @ $20/MWh | 77.2391 | 151.0844 | 89.8525 | 131.5594 | 123.569 | 416.8973 | 436.3585 | 730.8095 | 720.8133
24 h storage capacity
1 charge-discharge cycle per day
DoD 50%

## Slide 13
Siemens relations
Siemens has partial ownership of IP for HT-TES
Fundamental aspects of HT-TES invented by Stiesdal while serving as CTO of Siemens Wind Power; IP owned by Siemens
Key aspects of Brayton cycle and storage unit invented and owned by Stiesdal as independent operator
Siemens has position as observer and, on a case-by-case basis, consultant on Stiesdal’s activities on HT-TES
Siemens is interested in discussing license arrangements for Siemens-owned technology
Siemens is also interested in discussing equipment supplies (compressors, turbines, generators, switchgear, control systems, etc.)

## Slide 14
Thanks for your attention
Henrik Stiesdal
hst@stiesdal.com