## Slide 1
Life Cycle Assessment
Assessing local impacts
María del Mar Pintor
MsC Civil Engineer
The research leading to these results has received funding from the European Union Seventh Framework Programme under the agreement SCP2-GA-2013-614020.

## Slide 2
1.1 LCA METHODOLOGY
1. INTRODUCTION
LCA is a standardized technique to assess the environmental aspects and potential impacts associated with a product, process, or service.
The LCA process is a systematic, phased approach and consists of four components
Goal
and scope
definition
Inventory
analysis
Impact
assessment
Interpretation
Direct applications:
Product development
and improvement
Strategic planning
Public policy making
Marketing
Other
Life Cycle assessment framework
ISO 14040
ISO 14041
ISO 14042
ISO 14043
©2016 ACCIONA Infrastructure. All rights reserved.

## Slide 3
1.1 LCA METHODOLOGY
1. INTRODUCTION
- Assess the potential human and ecological effects of all inputs identified in the inventory analysis
Identify and quantify: energy, materials and environmental releases (air emissions, solid waste disposal, waste water discharges)
- Define the product, process or activity
- Establish the context
- Identify the boundaries and environmental effects
Goal
and scope
definition
Inventory
analysis
Impact
assessment
Interpretation
Evaluate the results of the inventory analysis and impact assessment
Select the preferred product, process or service with a clear understanding of the uncertainty and the assumptions considered
©2016 ACCIONA Infrastructure. All rights reserved.

## Slide 4
1.2 LIFE CYCLE STAGES
1. INTRODUCTION
©2016 ACCIONA Infrastructure. All rights reserved.
LCA is a “cradle-to-grave” approach for assessing innovative processes or products
Raw material acquisition
Production
Use
/
Reuse
/
Maintenance
Recycle
/ Waste treatment
INPUTS
OUTPUTS
Raw
materials
Air emissions
Water waste
Solid waste
Coproducts
Others
Energy

## Slide 5
2. LCA TOOL. GABI 6 SOFTWARE
©2016 ACCIONA Infrastructure. All rights reserved.
Provided by PE International, in collaboration with IKP University of Stuttgart
The program incorporates its own database with information of many processes
It includes Ecoinvent, GaBi and ELCD databases (update 2016)
Latest upgrade: Gabi 6

## Slide 6
3.1 SCENARIOS
3. CASE STUDY
©2016 ACCIONA Infrastructure. All rights reserved.
DESIGN SCENARIOS |  |  |  | 
 | Site conditions |  | Ground conditions | 
Design case | Water depth (m) | Distance to Port (km) | Shallow bedrock | Medium dense sand
0 | 20 | 30 |  | 
1 | 40 | 30 | Gravity bases | XL Monopiles Gravity Bases
2 | 60 | 100 | Lattice Structures Gravity Bases | Lattice Structures Gravity Bases
3 | 100 | 30 |  | Floating foundations
Site 1 | Location | Ground conditions | Foundation type | Foundation installation | Foundation Installation Vessel | Turbine Installation | Turbine Installation Vessel | Turbine Installation Method
 | West Gabbard | Shallow bedrock | Gravity base | Float-out | 3 tugs + 1 AHT + 1 support vessel | Installed separately | Jack-up | Bunny ears with 2 part tower

## Slide 7
3.2 FUNCTIONAL UNIT
3. CASE STUDY
©2016 ACCIONA Infrastructure. All rights reserved.
Reference product: Gravity Base Foundation
Function: Support of 8 MW Wind Turbine
Data gathering
from results of WP2
Geometry
Bottom slab | 28 m diameter
Shaft | 20 m height
Footing | 31 m diameter, 1 m thickness
Transition piece | 24 m height; 8 m diameter; 75 mm thickness
Outer perimetral wall | 50 cm thickness
Inner perimetral wall | 30 cm thickness
Radial wall | 25 cm thickness
Inner cylinder | 1 m thickness; 8 m diameter
Composition
Concrete volume HA-35 | 3,498.33 m3
Steel quantity B500S | 524,749.5 kg

## Slide 8
3.3 PRODUCTION PROCESS
3. CASE STUDY
©2016 ACCIONA Infrastructure. All rights reserved.
1
Assembly of the bottom slab reinforcement
2
3
4
5
6
Concreting of the bottom slab
Placing of the first section of shaft reinforcement
Concreting of the shaft
Preparation of the launching
Launching and refloating of the floating dock
7
Concreting of top slab
9 days

## Slide 9
4. INPUTS TO BE GATHERED. LCI
©2016 ACCIONA Infrastructure. All rights reserved.
Life cycle inventory (LCI)
Raw materials
Energy consumption
Reinforced concrete C-35
3,498.33 m3
Mass concrete C-20
1,107.42 m3
Steel B500S
524,749.5 kg
Water
598,214.43 kg
Demolding
3 m3
Cement
1,329,365.4 kg
Floating dock
26,853.12 kW·h
1 Crane
1,296 kW·h
Transport
1 Tug
48,000 kW·h
Worksite facilities
2,160 kW·h
1 tn Crane
80 km
Concrete pumps (12 tn MAM)
40 km
Material storage (12 tn MAM)
300 km
Product: Caisson
11,697.700 tn

## Slide 10
5. SIMULATIONS AND LCA RESULTS
©2016 ACCIONA Infrastructure. All rights reserved.
Environmental impacts | Stage I | Stage II | Units
 | Value | Value | 
Global Warming Potential (GWP 100 years) | 485 | 1250000 | [kg CO2-Equiv.]
Acidification Potential (AP) | 2,03 | 2360 | [kg SO2-Equiv.]
Photochem. Ozone Creation Potential (POCP) | -0,68 | 326 | [kg Ethene-Equiv.]
Eutrophication Potential (EP) | 0,51 | 275 | [kg Phosphate-Equiv.]
Primary Energy Demand (PED) | 6680 | 8270000 | [MJ]
Conclusions
Comparison with XL Monopile
LCA in 2 stages:
  Stage I: Installation and mobilization of equipment
  Stage II: Caisson construction
Software tool: GaBi 6
  Legislation: EN15804 (Sustainability of Building Materials)
  Methodology: CML2001

## Slide 11
The research leading to these results has received funding from the European Union Seventh Framework Programme under the agreement SCP2-GA-2013-614020.
©2016 ACCIONA Infrastructure. All rights reserved.

## Slide 12
Thank you very much
for your attention