## Slide 1: The supply chain’s role in the journey to ‘subsidy free’
Giles Hundleby
Hamburg
27 September 2016

## Slide 2
  Journey to ‘subsidy free’ – why it’s important
  It’s not just about technology
  Progress this year…
  LCOE reductions and role of the supply chain
  Beyond subsidy free
  Conclusions
Contents
Agenda
The supply chain’s role in the journey to ‘subsidy free’
Selected clients
BVG Associates
Business advisory
Analysis and forecasting
Strategic advice
Business and supply chain development
Technology
  Engineering services
  Due diligence
  Strategy and R&D support
Economics
  Socioeconomics and local benefits
  Technology and project economic modelling
  Policy and local content assessment

## Slide 3
1. Journey to ‘subsidy free’ – why it’s important
Going slow is not an option…we could already see in 2015 that costs were falling fast
  .
Cost of Energy Reduction = Offshore Wind Subsidy free by ‘23

## Slide 4
2. It’s not just about the technology….
Supply chain, cost of finance and technology improvements together deliver LCOE reductions
Innovations in Technology by wind farm element
Supply chain and finance
Anticipated LCOE reductions from 2015 to 2030 – fixed 2015 €

## Slide 5
3. Progress this year has been faster than expected
The Borssele auction brought forward technology, supply chain and finance benefits
Supply chain

## Slide 6
Turbine | Foundation & tower | Transmission | Installation | OMS | Development
Technology contributions to reducing LCOE |  |  |  |  | 
10% | 1.5% | 3% | 1.5% | 2% | 2%
Supply chain contributions to reducing LCOE |  |  |  |  | 
2% | 1.5% | 2% | 1.5% | 1% | 1%
4. LCOE benefits summary by element
What progress needs to be made?

## Slide 7
Turbine | 2016 | 2025 | LCOE benefit
Technology | 164m rotor 8MW @ 10rpm Ongoing development through life | 200m rotor 11MW @ 8rpm More intense initial development A few evolutionary ‘steps’ through life | 10%
Supply chain | Short pipelines Short-term supply contracts | Longer pipelines Long-term supply arrangements Additional investment in manufacturing quality and efficiency | 2%
4. LCOE reductions and role of the supply chain
What progress needs to be made?
Turbines
      Main per MW benefits
      Decreased foundation and installation CAPEX
      Decreased OPEX
      Increased energy production

## Slide 8
Foundation & tower | 2016 | 2025 | LCOE benefit
Technology | XL monopiles up to 35m and 8.xMW Pin-piled 3 and 4-legged jackets | Monopile use pushed further (up to water depths of 50m?) Jackets 3-legged and use pin-piles or suction-buckets | 1.5%
Supply chain | Tower and foundation designed separately Short pipelines/split supply Some standardisation | Integrated design of structure and standardisation Longer pipelines and supply arrangements Investment in manufacturing quality and efficiency | 1.5%
4. LCOE reductions and role of the supply chain
What progress needs to be made?
Foundation and tower
      Main per MW benefits
      Decreased CAPEX

## Slide 9
Transmission | 2016 | 2025 | LCOE benefit
Technology | Up to 100km: 220kV HVAC and 1-2 substations Beyond: 800kV HVDC with collector platforms and offshore substation | HVAC beyond 100km through low frequency, intermediate corrector stations and up to 400kV Lightweight structures | 3%
Supply chain | Custom design for each wind farm Some use of modules Single project pipelines | Standardisation of some designs Increased use of modules Multiple project pipelines | 2%
4. LCOE reductions and role of the supply chain
What progress needs to be made?
Transmission
      Main per MW benefits
      Decreased CAPEX

## Slide 10
Installation | 2016 | 2025 | LCOE benefit
Technology | Jack-up vessels for foundation installation and turbine installation (5-lift strategy) Capable vessels, but not optimised | Reduced sensitivity to weather, better risk management, optimised fleets and scheduling. Greater use of floating DP2 vessels for foundation installation | 1.5%
Supply chain | One project at a time, new PM team & build-out port Custom hardware | Vessels contracted for pipelines of projects Fewer build-out ports Re-use of most hardware from project to project | 1.5%
4. LCOE reductions and role of the supply chain
What progress needs to be made?
Installation
      Main per MW benefits
      Decreased CAPEX
      Decreased cost of capital

## Slide 11
OMS | 2016 | 2025 | LCOE benefit
Technology | Scheduled maintenance Some condition-based, but mostly reactive service | Full health and usage management Fully condition-based service with active health management Improved forecasting | 2%
Supply chain | Turbine suppliers, developers in-house and 3rd-party service providers Contract ranges from 1-15 years (turbine) | In-house monitoring and data control by owners Emergence of integrated 3rd part service suppliers Portfolio approach | 1%
4. LCOE reductions and role of the supply chain
What progress needs to be made?
Operations, maintenance and service
      Main per MW benefits
      Decreased OPEX
      Increased AEP

## Slide 12
Development | 2016 | 2025 | LCOE benefit
Technology | Met mast and some LiDAR Manually optimised layouts supported by CFD | Multiple floating LiDAR Improved wind resource measurement and wind farm layout | 2%
Supply chain | Projects developed in isolation Developer uses a mix of 3rd party suppliers Developments often don’t lead to projects | Projects developed in pipelines Increase in use of Dutch ‘Borssele’ model (government undertakes and shares site characterisation) | 1%
4. LCOE reductions and role of the supply chain
What progress needs to be made?
Project development
      Main per MW benefits
      Decreased CAPEX
      Decreased risk and cost of capital

## Slide 13
Turbine | Foundation & tower | Transmission | Installation | OMS | Development
Technology contributions to reducing LCOE |  |  |  |  | 
10% | 1.5% | 3% | 1.5% | 2% | 2%
Supply chain contributions to reducing LCOE |  |  |  |  | 
2% | 1.5% | 2% | 1.5% | 1% | 1%
4. LCOE benefits summary by element
Supply chain benefits will play a significant role in reducing LCOE

## Slide 14
5. Beyond subsidy free…
Plenty more evolution but also disruption
Technology changes also drive supply chain changes
      Aero control Float-out-and-sink Floating Multi-rotor Kites
      Huge blades need Avoid offshore crane cost Access new areas Better use foundations Aim higher
      better control
      Main per MW benefits
      Increased AEP Decreased installation CAPEX Increased AEP Decreased CAPEX Decreased CAPEX
      Decreased OPEX Decreased OPEX
Turbine supply chain
New supply chain?
Foundation supply chain
Turbine supply chain
New supply chain?

## Slide 15
  The journey to subsidy free is important
  Going slow is not an option…we could already see in 2015 that costs were falling fast
  It’s not just about technology
    Supply chain, cost of finance and technology improvements together will deliver the LCOE reductions
    Supply chain benefits will play a significant role
  Beyond subsidy free there will be more technology disruption and supply chain contribution to further LCOE reductions
Key points
Conclusions
The supply chain’s role in the journey to ‘subsidy free’

## Slide 16: Thank you
BVG Associates Ltd
The Blackthorn Centre
Purton Road
Cricklade, Swindon
SN6 6HY UK
tel +44(0)1793 752 308
info@bvgassociates.com
@bvgassociates
www.bvgassociates.com
The Boathouse
Silversands
Aberdour, Fife
KY3 0TZ UK
tel +44(0)1383 870 014
Green Garage
Second Avenue
Detroit, MI
48201 USA
tel +1 (313) 462 0673
This presentation and its content is copyright of BVG Associates Limited - © BVG Associates 2016. All rights are reserved.
Selected clients
BVG Associates
Business advisory
Analysis and forecasting
Strategic advice
Business and supply chain development
Technology
  Engineering services
  Due diligence
  Strategy and R&D support
Economics
  Socioeconomics and local benefits
  Technology and project economic modelling
  Policy and local content assessment