## Slide 1: Best Practice In Crane Transport Rigging and De-Rigging on Site by Dominic Murphy HSE Advisor Windhoist Limited Assisted By Declan Corrigan Technical Manager
Notes: Good Morning My Name Is Dominic Murphy and I am HSE Advisor Europe for Windhoist Limited,. Today I would like to talk to you about best practice in crane transport, rigging and de rigging on site.

## Slide 2
The wind industry has been the key driver in crane design & manufacture for the last 15 years.
Turbine hub-height has almost quadrupled & boom length will soon exceed 180m!
European policy and energy support mechanisms are changing radically.
We are being asked to optimise site infrastructure and reduce costs when the opposite should apply!
40m Hub-height to 160m!
Crane rigging & de-rigging
is more complex than ever
Notes: As turbines grow in size , so does the way they are manufactured, transported and erected on site. Crane manufacturers have adapted the size and versatility of cranes to suit this ever changing environment, however even though European policy is changing and adapting it still does not have a uniform platform for all to work with. Many countries have different rules and regulations with regards to movement of mobile cranes on our roads and as to what testing is required before, during and after pre erection and main erection. For example in France it’s a requirement to carry out overload tests every time the crane is configured. So from pre- erection to main erection, the crane would undergo , on a site with lets say 25 turbines, 50 overload tests for pre erection and 50 overload tests for main erection. Time consuming and totally unnecessary . In the UK we once had very strict overload testing practices, introduced in the 70’s however this has all changed. The UK Health and Safety executive repealed the Construction Operations 1961 ( specifically Lifting regulations) which stated that overload testing was required every 4 years. Since the introduction of LOLER – Lifting Operations and Lifting Equipment regulations 1998 overload testing became optional. The removal of overload testing in the UK has been led by industry. Many crane companies now work directly with the HSE and UK government to end Overload testing by releasing a TIN or Technical Information Note advising against it. As a Company we carry out full annual inspections on all our cranes and additional 6 month testing as a matter of course.

## Slide 3
Cranage is an integral constituent of our core activities.
Crane design has been tailored to suit optimised infrastructure design.
Our cranes operate at steep boom angles and our personnel work in, and under, suspended loads.
It is during transportation and mobilisation of cranes that we are exposed to greatest risk.
The law, and our obligations, is clear.
Moving cranes
Low-level work at height
Trucks moving crane parts
Notes: Mobile Cranes are an integral part of our core business and as these grow larger to keep up with ever growing turbine sizes , we are always mindful that all our operations are carefully planned and co-ordinated to ensure the safety of all our personnel and others working around our equipment . Good training and regular safety talks ensure that we have a accident free environment. However as good as this may sound it is not always the reality. Our cranes operate at steep boom angles and personnel are often exposed to Danger. For example whilst installing any tower section, nacelle, drive train operatives are often placed under large and heavy suspended loads. We always advise to steer clear of suspended loads however this is not always possible due to the nature of the build. Personnel are also exposed to danger during transport , rigging and de rigging of mobile cranes. Manufacturers make clear how to rig and de rig a crane and generally these guidelines are followed to the letter. Sometimes pressures from site management and above due to say inclement weather or delays to equipment delivery, mean that operatives will take unnecessary risks to bypass safety, in order to get the job done faster. Unfortunately this does result in incidents and accidents that we should not tolerate under any circumstance. The laws surrounding our obligations and requirements are very clear and are there to ensure we all go home at the end of our shift.

## Slide 4
WHAT MUST WE LEARN
An accident is classed as an unforeseen event.
If it is repeated then it is stupidity
When this happens we are (plural)
We have a duty to promote good practice.
The behaviour of personnel reflects the ethos of senior management!
Notes: Events, incidents accidents are unfortunate . Repeated events, incidents and accidents are more serious. We all have our own interpretation of the slogan ZERO HARM. In a speech recently it was said that if we can go one day, then two days then a week, a month, a year without incident why can it not be like this all the time. Well in an ideal world Humans would not make mistakes and equipment would not fail. We can provide our employees with the best training, best practice guidelines and best support possible, but as humans we have the ability to sometimes make choices that do fall within the good training received. We all have a duty to promote good practice and that message needs to come from the very echelons of the organisation.

## Slide 5
WHAT MUST WE DO
Ensure traffic management plans are simple and clear
Directions to site are followed precisely.
Ensure drivers do NOT use sat-navigation devices!
Notes: When we use subcontractors to assist with our site operations, we provide them with a clear traffic management plan that will ensure that all rules and regulations are followed; for example – Clear and concise directions and road numbers and given. Contact name and telephone number for use in emergency and to make contact at the agreed rendezvous point, to allow safe and escorted transit to site. However on this occasion the system broke down. Our subcontractor subcontracted the work out to another crane company and failed to pass on the very clear site instructions on how to get to the rendezvous point and who to contact. Instead the driver of the crane used his satellite navigation system that ultimately put him on a road that was not built to sustain the size and weight of his crane and ultimately giving way and rolling the crane 90 degrees . Luckily there were no injuries but a very bruised ego.

## Slide 6
WHAT MUST WE DO
Promote good behaviour!
Enforce basic rules e.g. phone use while driving?
6m
2.55m
This driver was sending an SMS
We cannot condemn this behaviour when we actually condone it!
Notes: On this particular occasion, the crane operator had finished de rigging his crane and was trying to make arrangements with his office on how he was getting home from site. After various failed attempts at calling his office, he resorted to sending text messages. He departed the hardstand and drove approximately 300 metres. Unfortunately for the crane operator, he was so busy using his mobile phone he drove his 140T crane off the site road. The site road was approximately 1000 metres long and dead straight. There should have been no excuses on this occasion. The use of mobile phones is strictly prohibited whilst driving on site.

## Slide 7
What happens when de rigging goes wrong
Notes: This accident was somewhat more serious. During the de rigging of out Terex TC2800 lattice boom crane, one of our crane technicians received serious injuries to his right hand . In this image you can see the crane drivers view of the boom. The boom is approximately 98 metres long. ( This model crane has a remote control unit that the crane driver can use on the move. On this particular model it was not installed) At the opposite end of the boom there are 2 crane technicians getting ready to assist the crane driver with hoisting in ( reeling in ) the hoist rope. This process calls for 2 crane technicians, one in constant communication with the crane driver and the other manually lifting the hoist rope. This is a safe process if done correctly. However this was not the case on this occasion. We carried out a recreation of the accident in our extensive investigation which I will play for you all now.

## Slide 8: What happens when de rigging goes wrong

## Slide 9
WHAT MUST WE DO
Promote good behaviour!
Simple guidelines for rigging/de-rigging cranes?
Adopt a pan-European approach – be consistent!
Notes: The promotion of good behaviour on site is very important and as already mentioned it should come from the very top. In this image we observe a crane operator , approximately 4 metres off the ground, yet not wearing a harness. It is not standard practice for crane drivers/operators to have any form of working at heights training. Some companies put their staff through the GWO working at heights programme, however this training although good for a turbine technician is not really appropriate for a crane technician. Specific training on how to climb , rig and de rig a crane should be mandatory. As a company we have developed a specific training programme that instructs crane drivers and crane technicians how to operate safely, on and around the equipment they are using. We should have a set standard throughout the industry, and certainly on all sites, UK Europe,Asia ,Americas in which mobile cranes are used to erect wind turbines. The sooner Manufacturers, Site PCs and clients get together and standardise site rules and regulations irrespective of country and safety culture the better it will be for all.

## Slide 10
WHAT MUST WE DO
Campaign for adequate site infrastructure!
Road running surface
Underfoot conditions
Adequate
Road
Width?
Road bearing capacity
Good quality civil works
Hardstand bearing finish
Notes: Lastly, as cranes grow in size, site infrastructure has to take this into account. Site roads are often inadequate, too narrow with poor edge protection. Hardstands vary from civil contractor to civil contractor. There are very good ones and there are very poor ones. As in the image you can see that the crane pads are not flush to the ground. This could seriously affect the cranes stability and performance during a heavy lift. Site roads are often difficult to navigate in wet weather, especially where steep slopes are extremely wet and slippery. Heavy transport often struggles to maintain deliveries and has been known to stop altogether, blocking site roads. This now presents a problem in case of an emergency – Access to essential emergency vehicles would be blocked creating a serious problem. Wider roads with more passing places would be an advantage were possible. Again a set standard would be advantageous.

## Slide 11: Thank you for listening
Any Questions