## Slide 1: Forecasting Wind Energy Costs and Cost Drivers The Views of the World’s Leading Experts Wind Europe 2016 | IEA Wind Task 26
This work was funded by the Wind & Water Power Technologies Office, Office of Energy Efficiency and Renewable Energy of the U.S. Department of Energy under Contract No. DE-AC02-05CH11231.

## Slide 2: IEA Wind Survey of 163 of the World’s Foremost Wind Experts, Focused on Cost and Technology Trends
What
Expert survey
to gain insight on magnitude of possible future - cost reductions, - sources of reductions, - enabling conditions for continued innovation
Changes in LCOE from 2014 to 2020, 2030, and 2050 - excl. any subsidies - excl. grid interconnection costs outside plant boundary
Onshore
Offshore
Fixed- bottom &
floating
Why
Inform
Policy and Planning, R&D, Industry investment and strategy
Improve
Treatment of wind in energy-sector planning models Complement
Learning curves, engineering assessments, and other tools
Who
Largest single expert elicitation ever performed on an energy technology in terms of expert participation
Familiarity with - Onshore Wind: 134 - Offshore fixed-bottom: 110 - Offshore floating: 44
- Europe: 100
Conducted under auspices of IEA Wind Task 26 on “Cost of Wind Energy”
163 Participants
(482 contacted)

## Slide 3: Expectations for Significant LCOE Reduction: Median “Best Guess” Scenario with Range of Expert Responses
Chart: 
| 40179 | 41640 | 43831 | 45658 | 47484 | 49310 | 51136 | 52963 | 55153 | 56615
 | -0.17096 | -0.2751 | -0.37924 | -0.40949 | -0.43974 | -0.46999 | -0.50024
 | 0.23514 | 0.087602 | -0.05994 | -0.10191 | -0.14388 | -0.18585 | -0.22783
median estimates | 0 | 0.06 | -0.25 | -0.38
Leading | -0.05 | -0.38 | -0.5
Chart: 
| 40179 | 41640 | 43831 | 45658 | 47484 | 49310 | 51136 | 52963 | 55153 | 56615
 | 0 | -0.15327 | -0.27351 | -0.39376 | -0.42222 | -0.45068 | -0.47914 | -0.5076
 | 0 | -0.04336 | -0.076813 | -0.11027 | -0.15548 | -0.20069 | -0.2459 | -0.29111
median estimates | 0 | -0.1 | -0.3 | -0.41
Leading | 0 | -0.15 | -0.35 | -0.51
Chart: 
| 40179 | 41640 | 43831 | 45658 | 47484 | 49310 | 51136 | 52963 | 55153 | 56615
Q3 | 0 | -0.14342 | -0.24576 | -0.34811 | -0.37555 | -0.403 | -0.43045 | -0.45789
Q1 | 0 | -0.052537 | -0.091985 | -0.13143 | -0.15775 | -0.18406 | -0.21038 | -0.23669
median estimates | 0 | -0.1 | -0.24 | -0.35
Leading | 0 | -0.13 | -0.27 | -0.48
2014 offshore baseline: 127€/MWh
Fixed-Bottom Offshore
Onshore
Floating Offshore
2014 onshore baseline: 59€/MWh
Lines/markers indicate the median expert response, range specifies 25th and 75th percentile
Leading experts (22) foresee greater LCOE reductions
For floating, change is shown relative to 2014 baseline for fixed-bottom
All dates are based on the year in which a new wind project is commissioned
Leading Expert Median Assessments

## Slide 4: In Absolute Terms, Narrowing Gap Between Onshore & Offshore, and Fixed-Bottom & Floating: Median Scenario
Lines/markers indicate the median expert response
LCOE reductions for floating offshore are expected to be especially sizable between 2020 and 2030
Chart: LCOE (€/MWh) in real 2014 Euros
| 2014 | 2020 | 2030 | 2050
FB bottom fill | 0 | 0 | 67.6692 | 50.3465 | 50.3465 | 26.3001 | 17.4797 | 0 | 0
Floating offshore | 169 | 180.23 | 131.6981 | 106.3402
Fixed-bottom offshore | 169 | 153.215 | 120.0788 | 102.6279
Onshore | 79 | 69.6618 | 58.3741 | 49.022
Note: Percentage changes from baseline are most broadly applicable approach to presenting findings (because each region & expert might have a different baseline value), but the relative absolute values of expert-specified LCOEs are also relevant

## Slide 5: How Will We Get There? Factor-Contribution to Median LCOE Reductions, 2014 to 2030
Absolute Change
in five factors
from 2014 to 2030 in median scenario
Capacity Factor: +4% (=47%)
Project life: +15% (=23 yrs)
CapEx: -14% (=3,008 € kW)
OpEx: -9% (=79 €/kW-yr)
WACC: -10% (=9%)
Capacity Factor: +9% (=49%)
Project life: +25% (=25 yrs)
CapEx: -5% (=3,308 € kW)
OpEx: -8% (=79 €/kW-yr)
WACC: -5% (=9.5%)
CapEx: -12% (=1157 €/kW)
OpEx: -9% (=40 €/kW-yr)
WACC: 0% (=8%)
Capacity Factor: +10%(=39%)
Project life: +10% (=24.5 yrs)
For floating offshore wind, change and impact are shown relative to 2014 baseline for fixed-bottom
Relative Impact
of five factor changes
from 2014 to 2030
in median scenario
on LCOE reduction
Chart: 
| CapEx | Capacity Factor | Financing Cost | OpEx | Project Life
Fixed-Bottom Offshore | 0.40414 | 0.15359 | 0.23011 | 0.059295 | 0.15287
Chart: 
| CapEx | Capacity Factor | Financing Cost | OpEx | Project Life
Onshore | 0.3599 | 0.38733 | 0 | 0.1076 | 0.14517
Chart: 
| CapEx | Capacity Factor | Financing Cost | OpEx | Project Life
Floating Offshore | 0.17831 | 0.34347 | 0.12705 | 0.062268 | 0.2889
Fixed-Bottom Offshore
Onshore
Floating Offshore

## Slide 6: CapEx & Capacity Factor Improvements Driven in Part by Growth in Turbine Size & Rotor Diameter: European Turbine Stats in 2030
All Regions
(not just Europe)

## Slide 7: Drivers for LCOE Reduction by 2030 Are Diverse: It’s Not Just Turbine Size
Survey asked about expected impact of 28 different technology, market, and other changes on LCOE reductions by 2030; Table shows top 5 responses for each turbine application

## Slide 8: Summary and Contact Information
  IEA Wind Task26 –
  Cost of Wind Energy
  Volker BERKHOUT
  Fraunhofer IWES
  volker.berkhout@iwes.fraunhofer.de
  Roberto LACAL ARÁNTEGUI
  European Commission Joint Research Centre
  Roberto.LACAL-ARANTEGUI@ec.europa.eu
  Ryan WISER, Joachim SEEL
  Lawrence Berkeley National Laboratory
  rhwiser@lbl.gov
For the full report on the survey results and a complete slide deck, see:
http://www.ieawind.org/task_26_public/task26_results.html