## Slide 1: Operational experience of wind turbines in cold climate
Nils Lehming
September 28th 2016

## Slide 2
Anti-Icing System - Features
Development of AIS
Validation of design and functionality
Field experience and yield improvement
Agenda

## Slide 3
Availability:
N117 Delta
N131 Delta
Heating element:
Electrical resistance heater
Carbon fiber reinforced plastics
Aerodynamically relevant surfaces
Operation:
Down to -20°C, even in severe icing
Fully operational during turbine operation
Power consumption:
Minimized by heating the surface rather than the blade structure
Minimized by intelligent algorithm to switch off, low power oder high power
Key features of the Nordex Anti-Icing System (AIS)
Nordex Anti-Icing System - Features
Anti-Icing System!
Fights the ice before it accumulates on the blade!

## Slide 4
Ice detection
Ice sensor
Meteorological conditions
Power output
Manual control
Smart control
Multi sensor approach:
Reliable ice detection is vital for a good Anti-Icing System
Nordex Anti-Icing System - Features

## Slide 5
Anti-Icing System - Features
Development of AIS
Validation of design and functionality
Field experience and yield improvement
Agenda

## Slide 6
Nordex has long experience in developing Anti-Icing Systems
Development
> 500 MW installed or in construction
2010: 3 x N100/2500-CCV-AIS with pilot Anti-Icing Systems
2011: 14 x N100/2500-CCV-AIS
2012: 32 x N100/2500-CCV-AIS
    2013: 1 x N117/3000-CCV-AIS
    30 x N100/2500-CCV-AIS
    2014: 9 x N100/2500-CCV-AIS
  34 x N117/3000-CCV-AIS
  2015: 2 x N131/3000-CCV-AIS
  17 x N117/3000-CCV-AIS
  2016: 13 x N131/3000-CCV-AIS (under construction)
  2017: 39 x N131/3000-CCV-AIS (contracted)

## Slide 7
Continuous improvement by learnings and innovations
Development
Experience/Improvements
2010
First AIS installed,
Technology Choice
Industrialization
Details improved
2011
2012
2013
2014
2015
2016
N100 (GRP blades)
Heat distribution,
manufacturing improved
Lightning protection improved (CRP blades)
N117 (GRP/CRP blades)
Ice detection improved
Maintenance simplified
Complexity reduced
N131(GRP/CRP blades)

## Slide 8
Anti-Icing System - Features
Development of AIS
Validation of design and functionality
Field experience and yield improvement
Agenda

## Slide 9
Dynamic flap wise: 2.5 million cycles
Dynamic edgewise: 7.5 million cycles
Validation – Structural design
Validation of design and functionality
NR65.5 blade is fully tested in static and dynamic tests applying all additional loads for the AIS
Static
Heating element

## Slide 10
Initial leader attachment test
High current coupon tests
Current distribution test
Validation – Lightning protection system
Validation of design and functionality
NR65.5 lightning protection system is fully tested by third party

## Slide 11
Resistance and insulation test
Inspection for Hot Spots
Heating cycles
Overheat protection test
Final acceptance test
Long time heating test
Validation – Anti-Icing System (AIS)
Validation of design and functionality
Every single blade of NR65.5 Anti-Icing System is fully tested in-house
Prototypes only

## Slide 12
Anti-Icing System - Features
Development of AIS
Validation of design and functionality
Field experience and yield improvement
Agenda

## Slide 13
Case Study: Performance in Different Ice Intensity Classes (Analyzed period Oct.2013-March 2014, N100/2500)
Production
+1.000 MWH
Production
+ 500 MWH
Required Energy
~50 MWH
Required Energy
~100 MWH

## Slide 14
Winter 2015/2016
N117/3000, Sweden
Field validation – Example of production gain in Lapland
Field experience and yield improvement
AIS OFF
AIS ON
Arctic Circle

## Slide 15
Power curves reflect the yield improvement due to Anti-Icing System (AIS)
Field experience and yield improvement
AIS OFF
AIS ON

## Slide 16
NORDEX Anti-Icing System …
… is based on proven technology
… is fully certified and tested
… has a long track record
… is subject to continuous improvement and innovation
… guarantees large yield improvement in icing conditions
Summary
Summary
Chart: Warranted Performance
| 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
Summer | 15 | 184 | 443 | 805 | 1298 | 1946 | 2727 | 3327 | 3580 | 3600 | 3600 | 3600 | 3600 | 3600 | 3600 | 3600 | 3600 | 3600
Active Icing | 12 | 147.2 | 354.4 | 644 | 1038.4 | 1556.8 | 2181.6 | 2661.6 | 2864 | 2880 | 2880 | 2880 | 2880 | 2880 | 2880 | 2880 | 2880 | 2880

## Slide 18
Nordex SE
Langenhorner Chaussee 600
22419 Hamburg
Germany
Tel: +49-40-30030-1000
Fax: +49-40-30030-1333
Email: info@nordex-online.com
Web: www.nordex-online.com
Acciona Windpower
Polígono Industrial
Barásoain, parcela 2
31395 Barásoain
Navarra, Spain
Tel: +34-948-720535
Fax: +34-948-720531
Email: infowindpower@acciona.com
Web: www.acciona-windpower.com