## Slide 1: Framework of Multi-Objective Wind Farm Controller Applicable to Real Wind Farms
J. Kazda, T. Göçmen, G. Giebel, M. Courtney, N. Cutululis

## Slide 2: Motivation
Wake effects cause up to 40% power loss and 80% increased fatigue loads in wind farms1
Optimal wind farm control (WFC) can potentially mitigate adverse wake effects2
Various optimal wind farm control approaches proposed in literature
Present wind farms do not use such control strategies
1 Sanderse, B. (2009). Aerodynamics of Wind Turbine Wakes: Literature Review. Energy Research Center of the Netherlands (ECN), ECN-E–09-016, Petten, The Netherlands, Tech. Rep, 46.
2 S. Barth, E. T. G. Bot, and H. B. Hendriks, “Evaluation of ‘ Heat and Flux ’ Farm Control,” Tech. Report. ECN-E-07-105, ECN, 2007.
Image source: Christopher Steiness
WFC
Operation set-point

## Slide 3: Objectives
Outline methodological framework of optimal wind farm controller that
  incorporates these solutions
  is applicable to real wind farms
  optimises the farm’s performance in all operation modes
Identify critical research areas in optimal WFC
Provide solutions
Compose solutions into control framework

## Slide 4: Overview of Optimisation Approaches in Optimal Wind Farm Control
Model-based optimal WFCs are composed of
  optimisation approach
  wind farm operation model
Commonly used optimisation objectives are
  maximisation of stationary total wind farm power output
  following of total power reference and reduction of turbine fatigue loading
Optimisation algorithms are extensively discussed in literature. These are
  non-linear optimisation techniques
  algorithms for linearized models such as linear quadratic control

## Slide 5: Validated, Advanced Wind Farm Operation Models Required
Present optimal WFC use wind farm operation models that are
  validated, static models originally derived for wind farm planning
  often extended for use in WFC, however seldomly validated
  estimate turbine fatigue loads using static loads
Future models should
  be validated experimentally
  include more environmental parameters such as turbulence intensity
  consider dynamics of wind farm operation such as wake meandering and fatigue loads
Overall, optimisation approaches need to consider relevant phenomena of dynamic wind farm operation

## Slide 6: Validated, Advanced Wind Farm Operation Models Used in Present Work
Wind farm controller in present work shall use validated, advanced models
Wind turbine loads are modelled based on HAWC2 tool
  HAWC2 is aeroelastic wind turbine simulation tool widely used in industry
SCADA-based estimation of wind farm power curve using PossPOW
  PossPOW is experimentally validated tool for real-time estimation of total wind farm power
  Validation performed both for normal and for downregulated operation of wind farm
  Estimate of wind farm power based on SCADA data

## Slide 7: Optimal WFC Designed as Add-on to Existing Infrastructure
Software architecture is aligned with communication norm of wind farm control
Active power controller of existing WFC
Other control
WFC add-on
PossPOW Tool
HAWC2-based turbine load model
Optimised turbine operation set-points
Wind farm active power operation mode
Sensor data
Other information

## Slide 8: Optimised Performance in All Wind Farm Operation Modes
Power maximisation
Balance control
Delta control
Abs. power limit
Power rate limit
Active power operation mode
Total power maximisation
WFC objective
Available power calculation using PossPOW
Power reference following with fatigue minimization
Base line
Actual
Operation change
Normal operation
Balancing services

## Slide 9: Flexible Software Architecture Provides Design Adaptability
Modular structure allows for easy adaptation of wind farm controller to different operator objectives and wind farm technology
Wind farm controller
Optimisation algorithm
Wind farm model
Measurement post-processing
Non-linear optimisation
PossPOW
HAWC2
Real wind farm sensors

## Slide 10: Summary
Controller add-on optimises wind farm performance in all wind farm operation modes with respect to
  total power
  turbine fatigue loading
Wind farm operation model shall use validated, advanced models, i.e. PossPOW and HAWC2-based turbine model
Norm compliant, modular design of wind farm controller add-on allows easy applicability to real wind farms

## Slide 11: Future Work
Testing of WFC using
  numerical wind farm simulation tools
  possibly full-scale wind farm
Vattenfall & Hasager, Charlotte Bay, et al. "Wind farm wake: The Horns Rev photo case." Energies 6.2 (2013): 696-716.

## Slide 12: DTU Wind Energy at WindEurope Summit 2016: Stand 574, Hall B6