## Slide 1
Offshore renewable energies: wave energy
Lesson 5

## Slide 2: In this course we will explore the different offshore renewable technologies:
What are renewable energy sources?
What is wind energy?
What is solar energy?
What is ocean current energy?
What is wave energy?
What is tidal energy?

## Slide 3: Waves transmit energy, not water
Lesson 5
Wave energy
Causes of wave formation
Wind
Barometric
Tidal
Seismic
Ships
Source: ElicaTeam, 2014. https://www.youtube.com/watch?v=NShUBfJQEHk&ab_channel=ElicaTeam

## Slide 4: Kinetic and potential energy of wave to generate electricity
Lesson 5
Wave energy
A wave energy converters device converts the kinetic or potential energy contained in sea waves to useful energy, mainly in the form of electricity.
Source: Magda Trzaska, 2023. Based on George Lemonis, Wave and Tidal Energy Conversion. Encyclopedia of Energy. https://www.sciencedirect.com/science/article/abs/pii/B012176480X003442

## Slide 5: Wave energy potential could meet all global energy demand
Lesson 5
Wave energy
29 500 TWh per year
25 350 TWh per year
theoretical potential of wave power*
world’s electricity consumption in 2022**
* Innovation Outlook, Ocean Energy Technology. IRENA, 2020
** statista.com

## Slide 6: Global mean value of wave power, P (kWm)
Lesson 5
Wave energy
Source: A. Martinez, G. Iglesias. Published by Elsevier, 2020. https://s100.copyright.com/AppDispatchServlet?publisherName=ELS&contentID=S136403212030681X&orderBeanReset=true

## Slide 7: 24.9 MW of installed capacity globally in 2022
Lesson 5
Wave energy
Source: Ocean Energy Systems, 2023. https://www.ocean-energy-systems.org/publications/oes-brochures/document/wave-energy-developments-highlights-2023/

## Slide 8: Technology to harness the wave power
Lesson 5
Wave energy
Oscillating water columns
compress air to drive an air turbine
Overtopping devices
use the potential energy of water that spills into a closed reservoir to subsequently drive a hydraulic turbine
Oscillating bodies
converters use different conceptualizations to transform wave motion between bodies (up/down, forwards/backwards, side to side) into electricity
Source (A and B): Magda Trzaska, 2023. Based on Computational Fluid Dynamics (CFD) Simulation for Designing Mooring Bitts Position at the Barge for Wave Energy Conversion (WEC) - Scientific Figure on ResearchGate. www.researchgate.net/figure/a-Oscillating-Water-Column-b-Overtopping-and-c-Oscillating-Bodies-OB_fig2_345411862
Source (C): Magda Trzaska, 2023. Based on Hydrokinetic Power Review - Scientific Figure on ResearchGate. www.researchgate.net/figure/] 3-An-attenuator-wave-energy-converter-Source-EPRI-2007-Used-with-permission_fig4_267566259

## Slide 9: Advantages of wave energy
Lesson 5
Wave energy
Renewable
Accessible
Economic advantages
No land damage
High potential
Clean
Reliable

## Slide 10: What is the catch with wave energy?
Lesson 5
Wave energy
Visually unappealing
Damage to marine life
Maintenance
Ship disturbance
High initial costs